## Slide 1
Some US Views on 100+ GHz Spectrum Use &
Active/Passive Sharing Issues
Michael J. Marcus, Sc.D., F-IEEE
Adjunct Professor, Department of Electrical and Computer Engineering
Principal Research Scientist, Institute for the Wireless Internet of Things
Northeastern University
m.marcus@northeastern.edu
www.northeastern.edu/wiot
N3JMM/7J1AKO
UKSPF
THz Spectrum Workshop
20 April 2022

## Slide 2: Spectrum policy impacts new technology and is just as real as Maxwell’s Equations for implementers of innovative technology
Both have large
impact on designs

## Slide 3: What is special about >100 GHz?
Spectrum above 100 GHz is the next frontier for wireless technology although it is very different than lower bands for several reasons:
  Atmospheric absorption is a major factor in propagation - particularly at low elevation angles
  Very small wavelengths permit complex antenna functions in moderate sizes and quasioptical antenna designs
    But all finite sized antennas must have some sidelobes
    Antenna designers can seek to move sidelobes to least harmful directions
    Extrapolating sidelobes from present commercial antennas in lower bands is not a good predictor of what can be achieved in sidelobe levels

## Slide 4: What is special about >100 GHz?
Compared to lower bands, contains a large number of molecular resonances necessitating higher density of passive bands and a greater fraction of bandwidth needed for important passive applications such as environmental sensing and radio astronomy
  Leads to unique spectrum sharing challenges
  EESS(p) problem is much more difficult than RAS because RAS use is almost always in high arid remote areas
Good reference on passive band issues:
https://www.nap.edu/catalog/21774/handbook-of-frequency-allocations-and-spectrum-protection-for-scientific-uses

## Slide 5: 100+ GHz Regulatory Issues
ITU Rules contain 10 “prohibited bands” in 100-275 GHz
Plus additional bands where passive services are co-primary but fielded and mobile uses are not allowed or are secondary
  Impact of passive allocations much greater than in other spectrum regions
5.340 All emissions are prohibited in the following bands:
… 100-102 GHz, 109.5-111.8 GHz, 114.25-116 GHz, 148.5-151.5 GHz, 164-167 GHz, 182-185 GHz, 190-191.8 GHz, 200-209 GHz, 226-231.5 GHz, 250-252 GHz
Number of 5.340 passive bands Fraction of spectrum in 5.340 bands

## Slide 6: What is special about >100 GHz?
To paraphrase US’ most famous bank robber:
  That’s “where the bandwidth is”
    Bandwidth for optical fiber-like rates on Fixed Service links
    Bandwidth for unique short ranges sensing applications
While it is unclear if/when >10 GHz BW may be needed for IMT uplinks and downlinks, but is likely needed for 5G and 6G backhaul in places where optical fiber is not practical due to installation cost and speed issues
  Emergency restoration of network capacity after a disaster or other severe damage damage is a key application

## Slide 7: Possible Active uses of >100 GHz
Fiber optic-like connectivity/latency
  FO is generally less expensive in hardware cost, but depending on locations can have high installation costs and longer installation times
  THz alternative may be advantageous for
    Temporary installations
    Emergency service restorations in disasters
    Locations where FO installation is very time consuming or expensive
Nondestructive testing applications involving “Terahertz Time-Domain Spectroscopy”
  Includes real time quality control for certain types of industrial manufacturing to increase yields
  Unusual imaging systems
    https://raysecur.com/mailsecur/

## Slide 8: Terahertz Time-Domain Spectroscopy https://en.wikipedia.org/wiki/Terahertz_time-domain_spectroscopy
Nontelecom use developed in the 1990s is short range (~1m) radar-like technology uses picosecond pulses to probe materials’ composition
  Useful for real time quality control in manufacturing
Continuous spectrum that spans 5.340 bands creates regulatory ambiguity and uncertainty for developers
  But products are now manufactured in several countries

## Slide 9: “The Chart”: Show available bandwidths with and without sharing with passive service
Horizontal
path
5opath

## Slide 10
States that sharing with passive is a goal if technical means can be found
  WRC-2000 version gives range as 71-275 GHz
  2019 update deals with 275-1000 GHz somewhat differently
“Take into account the principles of burden-sharing to the extent practicable”
  Both active and passive services should consider modifying their long term designs to facilitate sharing, e.g. antenna patterns
Any general permission for sharing, outside terms of RR4.4, requires action by a World radio Conference – held every 4 years
WRC-2000 Res. 731 https://www.itu.int/dms_pub/itu-r/oth/0C/0A/R0C0A00000F00149PDFE.pdf

## Slide 11: Interference/Sharing Scenario
In telecom almost all paths have low elevation angles
  Direct rays from such paths are severely attenuated by atmospheric absorption before they could reach a satellite
  But higher elevation sidelobes encounter much less absorption and can be interference threat
  Thus normal parabolic antennas or horns have unacceptable sidelobe levels for sharing, but other antenna approaches are possible
Front-haul
Wireless Back-haul
EESS
h (from ground)
𝛉
d
a (orbit)

## Slide 12: Approaches to Sharing: Suppression of high elevation angle sidelobes
Suppression of high elevation angle sidelobes with beamforming antenna arrays
Skyward
directions
Skyward
directions
Skyward directions
Skyward directions
Conventional beamforming arrays, MIMO systems
Denser beamforming arrays, refined MIMO systems
Optimize for the position of the nulls of power, not only the maxima

## Slide 13: Approaches to Sharing: Dynamic null steering as passive satellite crosses over
(Most) satellites can be precisely tracked (online, with free commercial tools), e.g.,
  Identify them here (sort by frequency): https://www.wmo-sat.info/oscar/satellitefrequencies
  Track them here: https://www.n2yo.com/database/
  Modify radiation pattern accordingly to minimize interference

## Slide 14: Approaches to Sharing: Mesh Network
Use a mesh network for back haul links
Compute sidelobe illumination over time of passive satellites from each potential link as satellites pass overhead
Route traffic in order to maintain total power at satellite antenna below ITU-R limits

## Slide 15: Propagation, Directional Antennas
d = 10 km, directional antenna
a = 408 km, directional antenna

## Slide 16: Recent mmW Policies in US & UK
Issue | USA | UK
Bands (Almost the same) | 116-123 GHz, 174.8-182 GHz, 185-190 GHz and 244-246 GHz | 116-122 GHz, 174.8-182 GHz and 185-190 GHz
Status | Unlicensed | Spectrum Access: EHF licence
Power limits (EIRP) Indoor | Average 40 dBm Peak 43 dBm; (Also allowed outdoors) | Peak 55dBm
Outdoor rules | Fixed outdoor use av. EIPR <82 dBm Reduced by 2 dB for every dB that the antenna gain is less than 51 dBi (55 dBi is beamwidth <1°, a 0.35m parabola at 116 GHz) | EIRP elevation angle mask Main beam elevation angle <20° above horizontal
https://www.ofcom.org.uk/__data/assets/pdf_file/0024/203829/100-ghz-statement.pdf
https://docs.fcc.gov/public/attachments/FCC-19-19A1.pdf

## Slide 17: Recent mmW Policies in US & UK Comments
Bands are almost the same
  US-only 244-246 GHz band is probably of little practical interest as 2 GHz BW bands are available at lower frequencies
Largest bandwidth is 7.2 GHz, less than present largest Fixed/Mobile allocation 151.5-164 GHz (12.5 GHz BW)
UK peak power limit 12 dB lower than US is puzzling
FCC’s outdoor limits using antenna gain to limit EESS(p) interference is naïve in that risk if generally from sidelobes peaks which have little to do with main lobe gain
  Ofcom’s eirp elevation angle mask is more expensive to measure but also a more effective predictor of interference potential

## Slide 18: Unique US Provision: Spectrum Horizons Experimental License
“The purpose of the flexible Spectrum Horizons Licenses is to incentivize the development of novel technologies for use above 95 GHz while preventing instances of harmful interference”
A new variant of experimental licenses with a 10 year term and ability to sell equipment and have license apply to purchasers – a “fast track spectrum access scheme”
User must propose use area
Rules do not preclude any specific frequency but requires 2 showings:
  License will not cause interference to any incumbent allocated users, e.g. EESS(p)
  If proposed spectrum includes a passive allocation, must show why sharing of the passive allocation is necessary

## Slide 19: Conclusions
The sharing of passive bands >100 GHz is a high payoff difficult technical challenge
  ITU rules clearly state sharing must meet specific cumulative protection levels at both passive satellites and radio astronomy facilities
  Opening these bands to controlled sharing will enable new technology for spectrum-based alternatives to fiber optics in special circumstances where fiber is not viable due to installation issues/costs
  Will also enable use of Terahertz time domain spectroscopy for nondestructive testing and enhancing manufacturing productivity
Let’s get the passive and active communities to cooperate with each other in good faith to pursue this challenge under the ITU’s guidelines in Res. 731
Do you want to learn more? M. Polese, X. Cantos-Roman, A. Singh, M. Marcus, T. Maccarone, T. Melodia and J. M. Jornet, “Coexistence and Spectrum Sharing above 100 GHz”, submitted for journal publication, August 2021
https://doi.org/10.48550/arXiv.2110.15187

## Slide 20
Thank you very much for your attention
Michael J. Marcus, Sc.D., F-IEEE
Adjunct Professor, Department of Electrical and Computer Engineering
Principal Research Scientist, Institute for the Wireless Internet of Things
Northeastern University
m.marcus@northeastern.edu
www.northeastern.edu/wiot
N3JMM/7J1AKO
With thanks to Prof. Josep M. Jornet
Department of Electrical and Computer Engineering
Northeastern University
Acknowledgement: With the support of the National Science Foundation, under the NSF Spectrum Innovation Initiative Planning Grant AST-2037896. We also thank M. Polese, X. Cantos-Roman and A. Singh @ Northeastern for their contributions to this body of work.