## Slide 1: West London facilitating connections
Tech UK & Data centres
December 2022

## Slide 2
Facilitating Connections within t constrained zones
Actual capacity being used by connected customers
Physical Network Capacity (T or D)
Assets on the network have a physical maximum rated capability (as per the blue column)
Each asset on the network will have a different capability (e.g. Transformers, cables, overhead lines)
Assets currently connected to our network are being utilised (as per the purple column)
It is important that the utilisation of the asset does not exceed the assets capability

## Slide 3
Facilitating Connections within t constrained zones
Actual capacity being used by connected customers
Physical Network Capacity (T or D)
When SSEN receive a request for a connection we assess the request, including maximum recorded capacity being used, to determine if it will remain within the physical network capability.
In this case (the green column), Customer 1 can connect without triggering reinforcement
Queue Customer 1

## Slide 4
Facilitating Connections within t constrained zones
Actual capacity being used by connected customers
Physical Network Capacity (T or D)
When SSEN receives another request for a connection we assess the latest request, including maximum recorded capacity being used and customer 1’s need, to determine if it will remain within the physical network capability.
In this case (the yellow column), Customer 2 would exceed the capacity of the asset capability and would trigger reinforcement; unless Customer 2 accepted a "Tipping Point" which would avoid triggering the reinforcement.
Queue Customer 1
Reinforcement triggered
Queue Customer 2

## Slide 5
Facilitating Connections within t constrained zones
Actual capacity being used by connected customers
Physical Network Capacity (T or D)
Under our current rules, when Customer 3 requests a connection they will have to wait for the reinforcement triggered by Customer 2, and any further reinforcement triggered by Customer 3 is completed before Customer 3 can connect.
Queue Customer 1
Reinforcement triggered
Queue Customer 2
Queue Customer 3

## Slide 6
Facilitating Connections within t constrained zones
Actual capacity being used by connected customers
Physical Network Capacity (T or D)
What our queue prioritisation tool is proposing is to offer Customer 2 the chance to either reduce their capacity requirement to connect within the networks capability until the reinforcement is completed; or
If Customer 2 is unable to reduce their capacity requirements, offer Customer 3 the ability to connect as their requirements can fit within the available asset capacity.
The overall reinforcement would still need to consider the requirements of all Customers in the queue, the current network usage and anticipated load growth to ensure we are not just building our network for what’s needed now.
Queue Customer 1
Reinforcement triggered
Queue Customer 2
Queue Customer 3
Reinforcement must, as a minimum, account for this need

## Slide 7: A range of solutions For West London connections
Trial to enable smaller demand customers to connect even where there are Tx constraints
Solution
Impact
Workstreams
<1MVA demand customers can connect without waiting for Tx reinforcement
Enable capacity ramping for demand customers who can phase build out
Demand customers who build out at <1MVA a year can connect without waiting for Tx reinforcement
Revised queue management process
Technical (developed with NGESO & NGET)
Reallocate physical Distribution capacity sterilised by customers waiting on Tx reinforcement
Working closely with Local Authorities to understand future development plans that impact networks i.e. housing
Identify where any Dx reinforcement is needed to accommodate new housing
Using LAEPs, we will deliver strategic network investment to develop the network for the future
Enable more strategic (anticipatory) investment in networks (with reg support)
Reallocating unused capacity to new connections projects
Provides additional capacity for connections in West London
Seeking flexibility services from existing customers in West London
Reducing peak network demand and enabling further connection
= Local Area Energy Plans (LAEP) input critical to success
Efficient use of network capacity
Solution
Impact
Workstreams
Technical (developed with NGESO & NGET)
Strategic network planning
Efficient use of network capacity

## Slide 8: 1MVA threshold walkthrough
Overview
Where there are Transmission Constraints:
If your connection is ≤1MVA you will not have to go through a Transmission Impact Assessment (TIA)
If your connection is >1MVA but you have the ability to phase your connection by ≤1MVA per annum you will not have to go through a TIA
If your connection is >1MVA and you do not have the ability to phase, you will have to go through a TIA
Key Note:
There may be Distribution related constraints that could mean some connections will be restricted below the <1MVA stated above. These timescales will be significantly earlier that the timeline for Transmission investment.