## Slide 1: TeraHertz (THz) Spectrum Workshop - bands above 86 GHz
Simon Pike
spectrum@simonpike.eu

## Slide 2
Simon Pike
Introduction
Why consider TeraHertz bands now?
  Technology advances make a wider range of applications feasible
    In particular, mobile backhaul and fronthaul
  Increasing scarcity of spectrum at lower frequencies
  Agenda items at WRC-23 and WRC-27 may make long-term decisions
  Bands above 100 GHz are being considered for 6G
Why ‘above 86 GHz’?
  86 GHz is the top of the 71-76 / 81-86 GHz fixed link ‘e-band’
  This is the highest frequency band for which there is an established commercial ecosystem
  Up to this frequency, the allocations to services are heavily used

## Slide 3
Simon Pike
Scope of this workshop
This workshop will focus on applications that radiate ‘over a distance’
  i.e. the applications that involve ‘co-existence’
  Given the atmospheric attenuation, it will not address space applications
  Current applications are towards the lower end of this frequency range
    What is the potential for these applications to use higher frequencies?
‘Non-radiating’ applications include:
  testing, inspection and materials characterisation
  - e.g. the thickness of coatings
  - These typically operate closer to 1 THz
  - And use technologies that may not be readily ‘commercialisable’
  - Low transmit power or high cost
  Ultra high speed wireless busses within IT equipment
  Medical diagnosis

## Slide 4
Simon Pike
Free space path Loss
Free Space Path loss = Pr/Pt = Dt.E. A/4πr2
r = length of radio path
A = aperture of antenna (area
E = Efficiency of aperture capturing incident RF
Dt = Directivity, or ‘gain’, of transmit antenna
r
A
This equation is independent of frequency, BUT:
The directivity of an antenna of a given aperture increases with frequency2
The aperture of an array antenna of fixed complexity (number of elements) reduces with frequency2

## Slide 5
Simon Pike
Atmospheric attenuation
Relative humidity rarely drops below 50% in UK
But the absolute density of moisture in air drops at low temperature
Attenuation by other atmospheric gases is insignificant
Except at 60 GHz and 120 GHz - due to oxygen
Attenuation due to Rainfall is 12-15dB/km for 30mm/hour at >80 GHz
Typical 0.01% time in UK

## Slide 6
Simon Pike
Output Power of THz solid-state integrated sources
TeraHertz Monolithic Integrated Circuits
Resonant Tunnelling Diode Oscillators
Uni-travelling carrier photodiode photomixers
Mixing two optical wavelengths using a non-linear semiconductor device
Source: Resonant Tunnelling diodes high speed terahertz communications – a review https://eprints.gla.ac.uk/263093/ (Jan 22)

## Slide 7
Simon Pike
An example of mobile industry thinking (not an endorsement)
Assumptions:
Line of sight
Fixed EIRP
100Gbps in 10 GHz bandwidth
cross-polarization with two parallel streams per polarization (i.e., 4x4 LoS-MIMO).
Source: ITU-R WP5D Draft Working Document Towards a Preliminary Draft New Report ITU-R M.[IMT.ABOVE 100 GHz]

## Slide 8
Simon Pike
Speakers today
Introduction and propagation characteristics | Simon Pike
Ofcom's perspective W & D bands an operator perspective TeraHertz RF technology for W & D bands | Richard Moore, Ofcom Dave Townend, BT Dr Tudor Williams, Filtronic
Mobile industry perspective on TeraHertz bands | Reza Karimi, GSA
International activities | Simon Pike
Passive meteorological applications | Stephen English, European Centre for Medium-Range Weather Forecasts
US perspective | Michael Marcus, Northeastern University
Conclusions and next steps |