## Slide 1: LFT asymptomatic testing guidebook
VERSION 2.5

## Slide 2: PURPOSE OF ASYMPTOMATIC TESTING
OFFICIAL – SENSITIVE – COMMERCIAL
The purpose of asymptomatic testing is to identify individuals within the population who are positive for COVID-19 but do not present symptoms.
Identifying asymptomatic positive cases and informing them to self-isolate will reduce the spread of the virus.
Your organisation will use Lateral Flow Devices(LFD) to test Participants for coronavirus who are not displaying symptoms.
The government will be publishing findings related to LFD here:
https://www.gov.uk/government/publications/evidence-on-the-accuracy-of-lateral-flow-device-testing
This page will be kept up to date with findings and research papers from the DHSC.
TEST TYPE | HOW IT WORKS | SUITABILITY | SAMPLE TYPE | ANALYSIS TIME
Lateral flow test | looks for parts of the surface of the virus (antigen) | Asymptomatic participants | Throat and nose | 30 mins
Rt-PCR test | PCR Test - looks for the virus’s genetic material (RNA) | Symptomatic participants To confirm positive LFD results | Throat and nose Double nasal | Up to 2 days
OVERVIEW:
Asymptomatic testing sites are set up solely for testing asymptomatic test participants.
Any test Participants, or site staff, displaying symptoms of COVID-19 should leave the site immediately and follow the national guidance for getting tested. More information can be found here:
https://www.gov.uk/get-coronavirus-test

## Slide 3: TESTING PROCESS OVERVIEW
OVERVIEW:
ENGAGE EMPLOYEES
SET UP TESTING SITE & TRAIN STAFF
ORDER TEST KITS & PREPARE FOR TESTING
CONDUCT TESTING
TEST SAMPLE ANALYSIS
RESULT NOTIFICATION & FOLLOW UP
Procure services and materials described in this Guidebook
Identify the space for your testing site and set up according to the Guidebook
Mobilise staff to perform Test Operative roles, and organise your employees for testing
Set up Sites and Test Operatives on the Results Logging Website
Fill out the Order Form to organise test kit delivery in advance
Sign the Schedule to agree to the Terms
Communicate booking slots to your employees
The collected samples are processed and analysed on site in the allocated area, results will be determined on the day
Your consenting employees will receive their results to the contact details they provide when they register
Inform your Employees of your testing site and its purpose, share related materials with them, explain the testing process and ask them to provide consent to participate in testing
Begin testing employees
Notes: E2e process in sub
Add training into 2

## Slide 4: SUPPORT CONTACTS CHEAT SHEET
ISSUE TYPE | NEXT STEPS | SUPPORT CONTACT DETAILS
I have supply and delivery issues or clinical questions relating to the SOP or similar. | Refer to their SOP, ATS Guidebook and local processes Organisations / testing sites should provide as much information as possible about the issue or incident, providing their site ID and any relevant details when escalating. | Testing.incidents@dhsc.gov.uk
I have issues with the LogResults website. | Refer to the “Digital” section of the guidebook Read the “technical support and troubleshooting guide” If your issue is not resolved, contact the Log ResultsSupport team | 0203 281 6468
I need to report adverse incidents. | Submit the spreadsheet either to their SPOC (such as a University SPOC overseeing several ATS, or an organization's SPOC overseeing several testing sites) or directly to integrator@dhsc.gov.uk by COP every Friday. | integrator@dhsc.gov.uk
I have questions about training. | Go to the “Workforce” section of the guidebook Read the training FAQs in the Workforce Appendix | testertraining@dhsc.gov.uk 0161 903 1032
I have a query about site materials from the DHSC approved supplier | Go to the “Site Layout Options” Section Read the guidance, complete the provided ‘Bill of Materials’ and contact “Speedy” | covidsupplies@speedyservices.com 01332 850 004 (Option 4)
INCIDENT MANAGEMENT & EVALUATION:

## Slide 5: REPORTING ADVERSE INCIDENTS
OVERVIEW:
Adverse incident reporting is a Medicines and Healthcare Products Regulatory Agency (MHRA) regulatory requirement, and all sites should record and report this as part of their day to day running. The team leader is responsible for reporting all adverse incidents to MHRA.
REPORTING INCIDENTS WHICH ARE RESOLVED LOCALLY:
The Site Manager will need to capture these incidents in a spreadsheet on a daily basis, submitting it to integrator@dhsc.gov.uk by COP every Friday
If your organisation manages multiples sites, consider having a single point of contact provide a collated log for all your testing sites
An example reporting template is available for use at testing sites titled ‘Incident Reporting Template’
IF AN INCIDENT CANNOT BE RESOLVED LOCALLY:
The incident should not be recorded. It should instead be escalated to the testing.incidents@dhsc.gov.uk immediately or as soon as possible
Examples of adverse incidents which should be escalated include something breaking during use i.e., a swab.
Organisations are required to record and report adverse incidents to MHRA.
INCIDENT MANAGEMENT & EVALUATION:

## Slide 6: GUIDEBOOK SECTIONS
The guidebook has six sections followed by an Appendix
CLINICAL PROTOCOL & POLICY:
Common for all use cases, it lays out the testing process as well the legal and clinical requirements organisations are required to meet
1
TEST KITS & LOGISTICS:
Information regarding the test kits themselves, their contents, method of ordering and storage conditions
2
SITE LAYOUT OPTIONS:
Testing site blueprints for different layout options available, as well as details on the ordering of the equipment required for site setup
3
WORKFORCE:
The roles and responsibilities required to run a site and some example workforce models for different site sizes, throughputs and available workforce sizes
4
5
DIGITAL:
Guidance on the use of the digital solutions included in the ATS model, the Lite Registration process and the Log Results app, as well as information on managed devices
6
COMMMS & ENGAGEMENT:
Guidance on the types of communications material that you may need to get your testing operation running.

## Slide 7: 1 Clinical, protocol and policy
VERSION 2.5
Clinical protocols
Testing Process
Self Administering A Swab Test
Results Interpretation
Test Results
PPE Guidance
Waste Management
SEE APPENDIX: Legal, Quality, Risk and issue management

## Slide 8: 1.1 CLINICAL PROTOCOLS

## Slide 9: REGULAR & DAILY CONTACT TESTING
Each testing site may choose to select and use one or both of the following testing types, which will determine the frequency of testing:
REGULAR TESTING:
This type of testing has been used at ATS sites across the country
Involves a group of asymptomatic participants getting tested regularly, at a frequency which will depend on their circumstances
DAILY CONTACT TESTING:
When identified as close contacts of a positive case, Participants can be given the option of undergoing daily contact testing instead of self-isolating
When a positive case has been found, close contacts will be required to test each morning for 7 days – the organisation is responsible for ensuring compliance
Individuals who continue to test negative will be able to operate as per the Covid-19 guidelines from their local authority
If a participant is unable to test on any of the 7 days (for example if the ATS site is closed on the weekend or the test Participant has time off work), they will be required to self-isolate until they are able to take another test
Both types of testing can be used in conjunction with each other i.e. Regular testing can be used to identify positive asymptomatic cases in Participants that have not been reported to NHS Test and Trace, and daily contact testing can be used to minimise the loss to productivity through preventing a daily testing close contact group’s need to self-isolate.
There are two types of test-to-find testing, both aim to find positive cases in asymptomatic patients:
Regular testing – the regular testing of members of an organisation to screen for positive cases
Daily contact testing - an alternative to self-isolation for the contacts of positive cases, involving daily testing
NOTE: USE OF DAILY CONTACT TESTING IS RESTRICTED TO ORGANISATIONS ACCEPTED UNDER THE DAILY CONTACT TESTING PROGRAM

## Slide 10: TEST TYPE COMPARISON
 | REGULAR TESTING | DAILY CONTACT TESTING
Trigger | Participant opts into the programme with agreed frequency of testing | Participant has been in contact with positive COVID-19 case
Testing frequency | Determined by setting (often once per week) | Daily for 7 days
Trace | Contacts of positive PCR cases are asked to self-isolate | If someone in a daily contact testing close contact group has a positive PCR case, the clock will restart on the 7 days of testing for their contacts
Duration | 30 minutes | 30 minutes, daily for 7 days
Logistics | Delivered through standard ATS | Delivered through standard ATS
Test kits | Innova - 25 kits | Innova - 25 kits
Clinical process | Participant self-swabs Operative processes test Operative reads results | Participant self-swabs Operative processes test Operative reads results
Digital process | Private sector, public sector, schools and universities: Participant registers on Lite Reg, at this stage the Participant indicates that they are undergoing regular testing Operative enters results through Log Results Website, or the App on a managed device Care homes: Operative registers user and logs results through self-assert website | Private sector, public sector, schools and universities: Participant registers on Lite Reg, at this stage the Participant indicates that they are undergoing daily contact testing Operative enters results through Log Results Website or the App on a managed device Care homes: Operative registers user and logs results through self-assert website
Comms | DHSC comms team creates comms which are shared with organisations Organisations are able to refine comms material received from DHSC | DHSC comms team creates comms which are shared with organisations Organisations are able to refine comms material received from DHSC
NOTE: USE OF DAILY CONTACT TESTING IS RESTRICTED TO ORGANISATIONS ACCEPTED UNDER THE DAILY CONTACT TESTING PROGRAM

## Slide 11: 1.2 TESTING PROCESS

## Slide 12: PROCESSING PREPARATION
PREPARE TUBE RACK:
The extraction tube is placed into the tube rack
1
Whilst Participants are completing their test kit registration, the Sample Processing Operative prepares the LFD cartridge, extraction tube and extraction solution on the table in front of them.
SOLUTION PREPARATION:
6 drops of the extract solution is added into the extraction tube. Do not let the extraction solution bottle touch the edge of the extraction tube. Only add 6 drops. The prepared tube rack is placed in front of the Participant’s test space. This is where Participants will place their used swabs. The extraction solution bottle should be decontaminated with anti-viral wipes between samples to prevent cross-contamination
2
TEST BARCODE PREPARATION:
A copy of the Participant’s unique test barcode should be placed on the back of the LFD cartridge
3

## Slide 13: SAMPLE COLLECTION
COLLECT TEST SAMPLE:
Upon entering the test space, participants hand their test kit barcode over to the Operative, complete online registration and take their own throat and nasal swab.
SAMPLE PROCESSING:
The Sample Processing Operative will then analyse the Participant’s test Sample
5
7
SWAB HANDOVER:
Participants will place the used swab (fabric tip first) directly into the extraction tube on the tube rack.
6
BARCODE AND TEST KIT REGISTRATION:
Participants should stick their other unique test barcode onto their registration card, and complete online registration of their test barcode.
At this stage participants indicate digitally whether they are taking part in daily contact testing or regular testing whilst registering their barcode
4

## Slide 14: SAMPLE ANALYSIS
SWAB PROCESSING:
The Sample Processing Operative will pick up the extraction tube and hold and press the swab head against the wall of the tube with force while rotating the swab for about 10 seconds. (This releases the antigen into the extraction solution from the swab head).
8
REMOVE SWAB:
The lower end of the tube is squeezed whilst the swab is removed (to remove as much liquid from the swab head as possible). The swab is then thrown away into a clinical waste bin, and the cap of the extraction tube is placed onto the tube.
9
LFD CARTRIDGE PROCESSING:
2 drops of the solution is squeezed onto the sample well of the LFD cartridge and the time of the test is recorded on the LFD (for example “HH:MM”).
10

## Slide 15: RESULTS ANALYSIS
RESULTS INTERPRETATION AND UPLOAD:
Examine the presence of coloured lines on the LFD and mark the results on the LFD with a permanent marker. Upload the results to the national Test and Trace database.
    ‘+’ mark for positives
    ‘V’ mark for invalid and void tests
    ’-‘ mark for negatives
12
RESULTS DEVELOPMENT:
The LFD cartridge is moved to the results processing area (for example, Table A) and the timer is started to track the development of the sample. Results can be analysed after 20-30 minutes.
11
    NEGATIVE RESULT
-
    INVALID OR VOID RESULT
V
V
    POSITIVE RESULT
+
+
FOR ILLUSTRATIVE PURPOSES ONLY
A

## Slide 16: 1.3 SELF ADMINISTERING A SWAB TEST

## Slide 17: SELF-SWABBING SAMPLE COLLECTION PROCEDURE
RECEIVING THE SWAB
Participants will be given a sealed sterile swab at the welcoming desk and will be directed to a sample collection booth from the check-in zone.
A crowd control system should be in place to ensure the Participant is only sent into a booth when the Sample Processing Operative is ready to receive the swab.
PREPARING PARTICIPANTS FOR SWABBING
The Participant should have been asked to avoid eating or drinking for at least 30 minutes before taking the test to reduce the risk of spoiling the test.
Before commencing swabbing, the Test Supervising Operative will explain the process to the Participant.
The Participant will also be informed that the swab may sometimes make them gag and they should use a sick bowl for any expectoration or vomit and guidance will be given regarding what to do with this if used.
YOUNG PEOPLE & CHILDREN
Young people aged 16-17 can self-swab
Children aged 12 to 15 may self-swab under supervision, while children aged 11 or under should be swabbed by parents / guardians.
!

## Slide 18: SELF-ADMINISTERING A SWAB SAMPLE
1
2
Participants will use hand sanitiser to clean their hands
They will look inside their mouth, and find their tonsils at the back of the throat. They can use the mirror to help.
Their tonsils, or where they would have been, (if they are removed) are where they will swab their sample.
The Participant should identify the soft, fabric tip of the swab its sealed, sterile packaging, peel open the packaging and gently remove the swab whilst taking care to not touch the soft, fabric tip of the swab
3
Participants will gently blow their nose into a tissue. Throw the tissue into the clinical waste bin provided.
This is so that they get rid of excess mucus.
4

## Slide 19: SELF-ADMINISTERING A SWAB SAMPLE
5
6
Put the same end of the same swab gently into one nostril until they feel a slight resistance (about 2.5cm up the nose). Rotate the swab 5 times and slowly remove it.
They only need to sample one nostril. If they have nasal piercings and are unable to remove the piercings in at least one nostril, they should not proceed with the test. They should contact their organisation or local NHS trust.
Holding the swab between fingers, they will open their mouth wide and rub the fabric tip of the swab over both tonsils (or where they would have been) at the back of their throat, at least 3 times on each site (they can use a mirror to help them do this). If the Participant is unable to take a throat swab, they can swab both nostrils instead.
Carefully remove the swab stick from the back of their throat.
7
They place their swab directly into the pre-prepared vial in the test tube rack.

## Slide 20: 1.4 RESULTS INTERPRETATION

## Slide 21: RESULTS INTERPRETATION
All results must be reported after 30 minutes of development
LFDs with positive lines that appear before 30 minutes can be reported after 20 minutes of development (positive results will not turn negative)
LFDs that appear negative after 20 minutes of development may still become positive, so they can only be declared as negative after 30 minutes of development
If a positive line appears after 30 minutes, it should not be reported as positive
Line C must be coloured to have a valid test result
    NEGATIVE RESULT
-
    INVALID OR VOID RESULT
V
V
    POSITIVE RESULT
+
+
Negative result:
Coloured line on “C” only
Invalid or void result:
No coloured line
on “C”
Positive result:
Any visible coloured line on “C” and “T”, which may be faint

## Slide 22: 1.5 TEST RESULTS

## Slide 23: WAITING AREA FOR TEST RESULTS
OVERVIEW:
If the site has a waiting area, there should be clear reinforcement of the requirements for 2m social distancing, wearing face coverings and other control measures throughout the end-to-end process.
There should be a robust process for assurance of these measures.
There should be a designated individual with the responsibility to ensure these measures are being adhered to and to collate a daily report on this.
Additional team members may be needed to manage the flow of people in this area and to answer questions when the testing Participant gets their result. This approach may be useful to direct Participants with a void result to take a new test immediately.
If giving the result in person, this needs to be delivered using a prepared script, and people will be advised to contact one of the NHS T&T nurses for further advice if necessary.
THE SCRIPT SHOULD INCLUDE:
Detail of the result (negative, void, positive)
Instructions on what to do for void results (retest LFD, register for home PCR)
Instructions on what to for positive results (go home immediately and follow self-isolation guidelines)
Travel advice for Participants
How to register for a confirmatory test
Organisations can set up waiting areas for their test Participants whilst they wait for their results. This is optional and can be set up if needed. The area should be designated for Participants to wait on-premises while results are processed, social distancing must be maintained in the area at all times.

## Slide 24: NEGATIVE TEST RESULTS
REGULAR TESTING NEGATIVE RESULT:
Participants can continue to interacting with their Organisation as usual and are informed of their next testing slot
Participants who return a negative test result do not need to self-isolate unless: a) they are symptomatic (they’ll need to book a different test), b) someone they live with tests positive (or has symptoms and has not been tested yet) or c) they’ve been traced as a contact of someone who tested positive.
DAILY CONTACT TESTING NEGATIVE RESULT:
Until they have tested negative for 7 consecutive days, the Participant will need to return the following day for testing. They will be able to interact with their organisation as normal provided they can prove their negative result
Once they have tested negative for 7 consecutive days, they will be able to return to their usual test cycle (if there is one in place), or to life as “normal” (remaining conscious of currently government social distancing and hygiene guidelines)

## Slide 25: VOID TEST RESULTS
INVALID OR VOID TEST RESULT:
Participants should be re-tested ASAP using an LFD test if they are near to the ATS and operationally feasible.
If their re-test result is still invalid or void, they must organise a test through the national testing service (https://www.gov.uk/get-coronavirus-test)
If the Participant has left the testing site and it is operationally more feasible, it is acceptable to retest with a confirmatory test after the first invalid result. Participants should be directed to go to www.gov.uk/get-coronavirus-test and choose ‘home testing’ (do not choose a testing site).
They can continue interacting with the Organisation until they receive their test results
While awaiting a follow-up test they’ll only need to self-isolate if: a) they are symptomatic (they’ll need to book a different test), b) someone they live with tests positive (or has symptoms and has not been tested yet) or c) they’ve been traced as a contact of someone who tested positive – this also applies to those who are part of a daily contact testing programme

## Slide 26: POSITIVE TEST RESULTS
GUIDANCE FOR PARTICIPANTS:
They should follow the instructions given to take the follow-up test. If not given instructions at the Testing Site, they should go to www.gov.uk/get-coronavirus-test to book a follow-up test. They should choose to visit a testing site (e.g. RTS/MTU/LTS) if possible, as it is faster than requesting a home test
Without a rapid confirmatory testing result, contact tracing will not be initiated quickly and this will impact on the overall effectiveness of the public health intervention
Until the Participant gets further advice they and everyone in their household must self-isolate immediately for 10 days. The 10 days begin the day after your test date. They should only leave home for their follow-up test. Care homes residents must self-isolate for 14 days.
Participants are encouraged to inform their Organisations if they get a positive result
GUIDANCE FOR ORGANISATIONS:
Organisations are responsible for taking action if one of their Participants informs them they have received a positive result
They will be encouraged to contact PHE and/or their local authority to seek guidance or support contact tracing
GUIDANCE FOR THOSE PARTICIPATING IN DAILY CONTACT TESTING (PARTICIPANTS AND ORGANISATIONS):
If a Participant tests positive, then all those who have been identified as contacts (including any new contacts of the participant) must begin their 7-day daily contact testing period again
Participants who return a positive LFD result must take a different follow-up test on the same day (or as soon as possible).

## Slide 27: RETURNING HOME
PARTICIPANTS SHOULD:
Travel home immediately, wearing a face covering, if possible, in their own vehicle, walking or cycling
If they are not able to do so they should arrange for a member of their household to pick them up
Positive cases should follow national guidance when travelling home
Asymptomatic contacts of positives cases should go home as they would normally do. If the contact becomes symptomatic, they should follow same travel advice as positive cases.
It is especially important that people follow Government guidance on hygiene, including hand washing before leaving, throughout the process of attending a testing site.
Positive testing participants should be advised to return home as soon as possible following the provided guidance
POSITIVE TEST RESULTS:

## Slide 28: CONFIRMATORY TEST RESULTS
POSITIVE CONFIRMATORY TEST RESULT:
Upon receiving a positive confirmatory result, the Participant should self-isolate and follow the latest government guidance from the date of their latest test, before they can return to usual activities in line with government guidance
NEGATIVE CONFIRMATORY TEST RESULT:
If their confirmatory test result comes back negative, the Participant is safe to return to usual activities in line with government guidance
They may return home or to work
POSITIVE TEST RESULTS:

## Slide 29: 1.6 PPE GUIDANCE

## Slide 30
Put on plastic apron, making sure it is tied securely at the back.
Put on surgical face mask, if tied, make sure securely tied at crown and nape of neck. Once it covers the nose, make sure it is extended to cover mouth and chin.
Put on eye protection if there is a risk of splashing.
PUTTING ON (DONNING) PPE Make sure you perform hand hygiene. Use alcohol hand rub or gel or soap and water. Make sure you are hydrated and are not wearing any jewellery, bracelets, watches or stoned rings. This is guidance for full PPE donning, some of the steps may not be relevant for certain roles. Role specific guidance for PPE for staff can be found in the workforce section.
Put on gloves.
You are now ready to enter the testing area.

## Slide 31
Remove gloves, grasp the outside of the cuff of the glove and peel off, holding the glove in the gloved hand, insert the finger underneath and peel off second glove.
Perform hand hygiene using alcohol hand gel or rub, or soap and water.
Snap or unfasten apron ties the neck and allow to fall forward. Snap waste ties and fold apron in on itself, not handling the outside as it is contaminated, and put into clinical waste
REMOVING (DOFFING) PPE Surgical masks are single session use, gloves and apron should be changed between test Participants. All used PPE must be discarded as category B clinical waste in the clinical waste bins. This is guidance for full PPE donning, some of the steps may not be relevant for certain roles. Role specific guidance for PPE for staff can be found in the Workforce section.
Once outside the testing area. Remove eye protection
Perform hand hygiene using alcohol hand gel or rub, or soap and water.
Remove surgical mask.
Now wash your hands with soap and water.

## Slide 32: 1.7 WASTE MANAGEMENT

## Slide 33: OVERVIEW
CONSIDERATIONS:
All waste from the site itself should be treated according to the waste categorisation for the item
Please be aware that waste management guidance may differ in the Devolved Authorities, so for those testing sites please seek local guidance regarding waste management.
The Environment Agency has published RPS C23 Incinerating specified healthcare wastes at a municipal waste incinerator: which can provide an option of disposing of these wastes via municipal waste incinerators, even if they do not have the appropriate waste codes on the permit.
Please be aware that it is not acceptable to store Chemical or Offensive waste for a prolonged period of time e.g. 72 hours and then dispose of via municipal route. Waste in these categories must be treated in accordance with the instructions above.
All areas have a waste management ‘Duty of Care’ and are responsible for undertaking a local WM3 assessment for the classification of the waste that they will generate (if not identified in the table), this assessment must be documented.
A Duty Care Waste Transfer Note must be completed before waste is removed from site and records kept for minimum of 2 years.

## Slide 34: WASTE CLASSICATION & MANAGEMENT
ITEM | SAMPLE | WASTE CATEGORISATION | EUROPEAN WASTE CODE (EWC) | LIKELY MANAGEMENT ROUTE / WASTE HIERARCHY | HEALTH TECHNICAL MEMORANDA (HTM) 07.01 PACKAGING | ILLUSTRATION (When using the first disposal option)
General Waste | Sandwich wrapper | Domestic/ recycling | 20 03 01 | 1st Option: Materials Recovery Facility 2nd Option: Energy from waste 3rd Option: Landfill | Not applicable | 
All packaging | Outer packaging on equipment | Domestic / recycling | 15 01 01 15 01 02 15 01 05 15 01 06 | 1st Option: Materials Recovery Facility 2nd Option: Energy From Waste 3rd Option: Landfill | Use existing municipal route | 
Swabs | Absorbent pads Vials Tissues | Chemical | 18 01 07 Plus 18 01 04 | 1st Option: Energy from Waste 2nd Option: Municipal Incineration 3rd Option: Clinical Waste Incinerator | 1st Option: Unmarked yellow neutral container/bag 2nd Option: White / clear container/bag 3rd Option: Tiger bag Do not use hazardous waste packaging | 
Cartridges / Devices | LFT cartridge | Chemical | 18 01 07 Plus 18 01 04 | 1st Option: Energy from Waste 2nd Option: Municipal Incineration 3rd Option: Clinical Waste Incinerator | 1st Option: Unmarked yellow neutral container/bag 2nd Option: White / clear container/bag 3rd Option: Tiger bag Do not use hazardous waste packaging | 
Personal Protective Equipment | Apron Face mask Gloves | Offensive | 18 01 04 | 1st Option: Energy for waste 2nd Option: Municipal Incineration 3rd Option: Landfill (last resort) | 1st Option: Tiger bag | 

## Slide 35: 2 TEST KITS
VERSION 2.5

## Slide 36: TESTING TECHNOLOGY
Innova Lateral Flow Antigen testing involves processing a throat and nasal swab sample with an extraction fluid and a Lateral flow device (LFD).
The LFD detects a COVID-19 antigen that is produced when a person is infected with COVID-19. If this antigen is present, then two coloured strips will appear on the LFD, indicating a positive result. Results can be analysed in 20-30 minutes after the sample is loaded onto the LFD.
The testing technology used in Innova test kits contains products derived from animal cells, this is in common with similar tests of its kind. During development, at no time have any component parts been tested on animals.

## Slide 37: INNOVA LFT ACCURACY
OFFICIAL – SENSITIVE – COMMERCIAL
Evaluations from Public Health England and the University of Oxford show LFD tests are accurate and sensitive enough to be used in the community and are suitable for identification of true positives in asymptomatic people and surveillance.
ACCURACY | DEFINITION | RESULTS (as of 12/2020) Based on ongoing review in real time for the Innova SARS-CoV-2 Antigen Rapid Qualitative testing
Specificity | The measure of how good the test is at detecting negative cases | 99.68% (i.e. a false-positive rate of 0.32%)
Sensitivity | The measure of how good the test is at detecting positive cases | Overall sensitivity of 76.8%. 95% sensitivity for those with high viral loads.

## Slide 38
INNOVA TEST KITS CONTENTS For illustration purposes only, the items you receive may look slightly different.
EXTRACTION SOLUTION
Used to prepare the swab before results analysis
LFD CARTRIDGE
Where the sample is analysed
SWAB
Inside a sealed wrapper (Swabs are latex free)
EXTRACTION TUBE
Where the swab is processed before the sample is analysed

## Slide 39: STORING TEST KITS AND REAGENTS
Regular temperature checks should be made to check that the conditions are within the manufacturer’s acceptable range. You should follow the storage instructions provided by the manufacturer.
REQUIREMENTS:
The LFD devices and reagents must be stored between 2˚C and 30˚C
LFD devices and reagents must be stored between 15˚C and 30˚C when used for testing and sample processing
LFDs must be kept out of direct sunlight
The shelf life of test kits is 24 months from the date of manufacture

## Slide 40
OTHER DHSC PROVIDED ITEMS For illustration purposes only, the items you receive may look slightly different.
Participant Registration cards
A reference card for the Participant to keep as a record of their test.
UNIQUE TEST BARCODES
Unique barcodes come in sets of 3 or 4. They are used to match Participants to their test sample. Barcode sets cannot be shared or re-used, they are unique to the individual Participant.
Barcode 1: For the Participant to stick onto their test registration card
Barcode 2: For the sample Processing Operative to stick onto the Participant’s LFD
Barcode 3 or 4: Spare barcodes in case the other barcodes are damaged (unused barcodes must be discarded – they must not be reused)

## Slide 41: 3 Site Layout options
VERSION 2.5
Options available
Comparison of site options
Considerations when setting up a site
Accessibility considerations
Example layouts
Site build & cleaning materials
Permanent site closure guidelines

## Slide 42: 3.1 OPTIONS AVAILABLE
A
Single Privacy Booth
Flatpack partitions, flooring as required, accessories, chair/tables and signage.
Modular and scalable from 1 to many.
B
Open Plan
Minimal specification desk screens (clinically and operationally advisable), taped floor makings, desk partitions (if required due to lack of space, enabling safe social distancing)
Modular and scalable from 1 to many.

## Slide 43: OPTION A: SINGLE PRIVACY BOOTH
OVERVIEW:
Offers privacy for testing and fully accessible (e.g., for wheelchair users)
Healthcare waste bins should be accessible by both Participants and staff
Can be combined with option 2 to provide privacy facility
Low throughput space requirements: Small or mid-size room suitable for the construction of a single or several booths
Flatpack partitions, flooring as required, accessories, chair/tables & signage. Deployed between 1-5 booths.

## Slide 44: SINGLE PRIVACY BOOTH
Use this layout to set up a single accessible privacy booth. Refer to the “5. Example layouts” section for examples of how to combine and scale this layout.
KEY FEATURES:
Flat pack self-assembled testing booth with built in panels for swab sample handover
Physical barrier between Participant and Test Operatives
Wheelchair accessible
Provides complete privacy for the Participant
Floor tape used to mark out barriers for Test Operatives

## Slide 45: FRONT PANEL DIMENSIONS
200mm

## Slide 46: OPTION B: OPEN PLAN
OVERVIEW:
Single or multi-table layout in an open plan space
Requires more space than a booth layout due to social distancing requirements
Chairs are required for the Participants to sit during testing (the height limitations of the protective screens do not allow for effective infection control if the Participants stand)
If space is limited, partitions can be provided to separate test stations and maintain effective infection control
Suitable for single room/office space, or large testing site area that can be demarcated with tape
Screen is clinically and operationally advisable but not mandatory
Note, can be combined with option 1 to provide privacy facility
Low throughput space requirements: Small room for single test and analysis table
High throughput space requirements: Large open test area for multiple tables
Desk screens, taped floor markings and partitions (if required). Scalable 1 to many stations.

## Slide 47: OPEN PLAN LAYOUT
Use this layout to set up an open plan testing area with partitions between Participants. See the “5. Example layouts” section for examples of how to combine and scale this layout.
KEY FEATURES:
Physical partition / barrier between Participants to remove the need for social distancing between test spaces
Floor tape used to mark out barriers
2m social distancing for Participants outside of the sample collection area to ensure effective infection control
Testing site staff should try to maintain 2m social distancing with each other where possible, however, social distancing can be reduced if they are wearing full PPE

## Slide 48
OPEN PLAN: DESK SCREEN DIMENSIONS
All external corners to be 5mm radius cut
4mm router cut slot
90 degree folds must be parallel
Stand must be stable with no wobble
All sharp edges to be deburred/finished to prevent risk of injury

## Slide 49
Factors | Option 1 – Single Privacy Booth | Option 2 – Open Plan
Space | Small space requirement | Flexible to space requirements
Typical Target Population | Small | Scalable as per number booths
Infrastructure | Partitioned booth, flatpack booth | Desk, taped floor markings, screen (clinically and operationally advisable), partitions if required
Privacy / Accessibility | Full privacy and wheelchair accessible | No privacy / accessibility in open plan model, unless combined with option 1
Build Requirement | Self-assembly | Self-assembly
Maximum Throughput Per Booth | Per 1 Booth Per Hour: 10 tests Per 8 hour day: 80 tests Assumption: 1 test per person - 6 mins | 
Supply Delivery Lead Time | Lead time dependent on level of required infrastructure, site location and customer priority. However, please leave a minimum of 5 days’ notice | Estimated lead time of <1 day
3.2 COMPARISON OF SITE OPTIONS

## Slide 50: 3.3 CONSIDERATIONS WHEN SETTING UP A SITE
TESTING SITES SHOULD BE:
Large enough to permit social distancing. 2m social distancing should try to be maintained at all times, however, can be reduced with complying with the requires PPE guidance.
Over 2.5m in height
One-way systems to manage the flow of people
Accessible to all test participants e.g., wheelchair accessible, ground floor location
Fully cleanable across all surfaces (e.g., hard, non-porous flooring)
With adequate supply of fresh airflow and/or a non-recirculation mechanical air conditioning system to reduce risk of transmission
With accessible washroom facilities, changing rooms and hand hygiene facilities (soap and water/appropriate alcohol-based hand rub)
With mains power or a temporary generator power supply
Adequately lit
Reliably connected to the internet connection for registration and result capture
With a legal agreement allowing testing operations (if space not owned by the organisation)
With secured storage spaces with spaces for 15-30 degree temperature control
Signed off from a Fire safety, health and safety, mechanical and electrical and security perspective
With an appropriate space for clinical waste bins, accessible by waste collection services
With an appropriate reception space to maintain social distancing

## Slide 51: SCALING & COMBINING THE BUILD OPTIONS
The site layout options are modular and scalable.
Organisations should build testing sites considering the number of booths required and the privacy needs, and scale accordingly.
Note that options can be combined. For example:
If a testing site needs an open plan, high throughput testing site with privacy facilities, they should combine options 1 and 2

## Slide 52: PARTICIPANT ARRIVAL AREA
WHAT IS THIS AREA:
The entrance to the testing site which can be indoors or outdoors
This area may contain a socially distanced queue system as appropriate for the organisation’s specific testing site location
The initial point of contact between the Participant and the testing site
FEATURES OF THIS AREA:
Demarcated one-way system for Participants
Hand sanitiser station(s) on entry / in arrival area
Check-in point or system to allow Participants to receive their test kit and bar code
FOR ILLUSTRATIVE PURPOSES ONLY

## Slide 53: TESTING STATIONS
WHAT IS THIS AREA:
The dedicated zone(s) on the site for the Participant to collect their swab sample
This area may contain a booth, table, a marked zone, or multiples of these depending on the organisation’s choice
It might be useful to reserve a test station for first time Participants, as they are likely to take longer to complete the testing process
FEATURES OF THIS AREA:
Hand sanitiser station(s) in the sample area
Testing guidance and supervision for Participants
A system for the Participant to pass their sample for analysis, such as a hatch or open space
Demarcated one-way exit route
ACCESSIBILITY:
The sampling area should have an accessible sample collection booth if required
FOR ILLUSTRATIVE PURPOSES ONLY

## Slide 54: PROCESSING & RESULTS AREA
WHAT IS THIS AREA:
The zone where Participant samples are received and analysed, where each device is developed until a result is available
The space where the results are recorded
FEATURES OF THIS AREA:
Desks for receiving and processing Participants’ samples
Access to PPE and hand sanitiser station(s) for testing site staff
Waste management for the used materials
FOR ILLUSTRATIVE PURPOSES ONLY

## Slide 55: 3.4 ACCESSIBILITY CONSIDERATIONS
PHYSICAL REQUIREMENTS
Wheelchair access, including wheelchair height for reception desks and boxes to deposit tests
Hearing Loops
Varied seating options for people with different physical needs (seats with arms, seats without arms etc.)
STORAGE REQUIREMENTS
Easy Read
Large Print
Braille
Translations
Clear Masks

## Slide 56: PHYSICAL ACCESSIBILITY CONSIDERATIONS
It’s critical to consider accessibility from the outset when setting up a site – both to avoid unnecessarily excluding people that need a test and to avoid a timely and possibly expensive refitting exercise to do so retrospectively.
The following slides detail a checklist for physical accessibility requirements for testing sites designated for use only by asymptomatic people. Social distancing requirements remain in place nevertheless. Please ensure that these points have been factored when designing the layout of the ATS.
1
OFFICIAL SENSITIVE – DO NOT SHARE FURTHER WITHOUT PERMISSION – SUBJECT TO LEGAL, REGULATORY AND POLICY REVIEW
BUILDING ACCESS:
How easy is it for users to get to your site?
  Is there accessible public transport to the testing site?
  Are the pavements leading to the venue in good condition with dropped kerbs?
  Are there accessible road crossings with warning texture and crossing systems?
Is there disabled parking at or near the testing site?
  How many spaces are there?
  Is it within 50 metres uncovered or 100 metres covered to an accessible entrance?
  Is there lighting from the accessible parking to accessible entrance?
Is the main entrance easy to recognise, which can be defined by a unique physical feature or colour?
  If dark outside, is there appropriate lighting?
Is the entrance accessible?
  If there is a ramp, does it have a levelled area at the top?
  If the doors are closed, can they be opened unaided by a person in a wheelchair i.e. lightweight door (try opening it with one finger), low door handle, or automatic button?
  Are steps and floor level changes clearly marked with a bright contrast edging?
Is there an entrance lobby where a wheelchair user can move clear of one door before using the next one?
  Does the lobby door have space to be fully opened?
  Is there a trip hazard?
  Is there a see-through, visual panel so you can see someone approaching?
Is there a reception area?
  Is there the reception desk at a suitable height for wheelchair users to see over?

## Slide 57: PHYSICAL ACCESSIBILITY CONSIDERATIONS
2
3
FACILITIES AND SERVICE:
Is there clear access to the testing area?
  Wide doors?
  Wide corridor?
  No obstacles in the way e.g. rubbish bin, etc…
  If the doors are closed, can they be opened unaided by a person in a wheelchair e.g. lightweight door (try opening it with one finger), low door handle, automatic button?
Is there colour contrasting in the building so that the doors and fixtures are easy to distinguish?
  Does the furniture contrast with the surroundings so that sighted and partially-sighted people can detect it and be less likely to bump into it?
Are the floor surfaces non-slip?
  Does the floor surface create a glare?
Is there hearing loop support at your site?
  Are staff aware of how and when to use hearing loops?
Is there a private assistance area for people who may need additional assistance with registration? e.g. non-digital / assisted digital areas?
  Is this area private / out of view for those who may not want to expose their need for support?
  Is this area accessible for wheelchair users?
  Does this area have basic furniture (table, chairs) that is both accessible and not causing an obstruction?
  Does this area have varied seated options for people with different physical needs (e.g. seat arms attached, no seat arms)?
Is there clear signage?
  Is only the first letter of each word capitalised?
  Is the font simple or plain, such as Arial or Helvetica?
  Is there colour contrasting, such as black & white or yellow & dark blue
EVACUATION PROCEDURES
What is the evacuation procedure for assisting wheelchair users out of the building?

## Slide 58: 3.5 EXAMPLE LAYOUTS

## Slide 59: MULTI OPEN PLAN LAYOUT EXAMPLE – WITH PARTITIONS
KEY FEATURES:
Example for 7 testing stations
Partitions remove the need for social distancing between testing stations, allows for more testing stations to be set up be set up in a smaller area
Participants follow a one-way system around the testing site to enter and exit
Test Operatives should wear full PPE as there is limited space for social distancing
May need extra partitions if Organisations want to reduce the social distancing space between the Test Operatives and the one-way walk-way for Participants

## Slide 60: MULTI OPEN PLAN LAYOUT EXAMPLE – WITH PARTITIONS

## Slide 61: MULTI OPEN PLAN LAYOUT EXAMPLE – WITH PARTITIONS - 3D MODEL

## Slide 62: MULTI OPEN LAYOUT EXAMPLE – NO PARTITIONS
KEY FEATURES:
Example for 6 testing stations
No physical barriers between Participants
Requires a much larger space than “partitions” as social distancing is required
Participants follow a one-way system around the testing site to enter and exit
Test Operatives have enough space to socially distance themselves

## Slide 63: MIXED LAYOUT EXAMPLE
KEY FEATURES:
Example for 6 testing stations (1 single Privacy booth and 5 open plan with social distancing)
Provides Participants a private testing space if they need one
Requires a larger space to set up
Participants follow a one-way system around the testing site to enter and exit
Test Operatives have enough space to socially distance themselves

## Slide 64: 3.6 SITE BUILD & CLEANING MATERIALS

## Slide 65: USING THE BILL OF MATERIALS
1
3
4
5
PLAN SITE LAYOUT:
Decide on the type of testing site layout using ‘Single privacy booths’, ‘open plan’ testing spaces or a combination of both and how many testing stations are needed. These are needed to calculate the type and quantity of testing site materials.
2
USE THE SPREADSHEET:
Open the latest Bill of Materials spreadsheet.
TYPE OF TESTING SITE:
Use the tabs at the bottom of the spreadsheet to see the list of materials needed for the different types of testing site layouts.
NUMBER OF TESTING STATIONS:
Enter the number of testing stations required for the chosen testing site layout. The spreadsheet will calculate the quantity of each item based on this.
ORDER MATERIALS:
Items in the Bill of Materials can either be; procured through Speedy (DHSC approved supplier, ordering process outlined on the following slide) or procured by the Organisation independently.
Check the “supplier” column in the spreadsheet to see who is responsible for each item. More information about ordering materials is available on the next page.
The Bill of Materials is a separate spreadsheet file that accompanies this Guidebook. It tells you what materials you need to run a testing site and calculates the quantity of each item based on the number of testing booths/spaces. This spreadsheet can be used as a reference to manage inventory levels. Screenshots overleaf show the quantities required for one testing station.

## Slide 66: OPTION A: BILL OF MATERIALS FOR SINGLE MODULE BOOTH
Single Module Booth Layout - Bill of Materials Please note distinction between Single Fill and Weekly level items. Replenishment items are expected to deteriorate over time and as such should be replaced as requried, but on no fixed cadence. |  |  |  |  |  | 
Key: User = customer e.g. University SOP = Standard Operating Procedure |  |  |  |  |  | 
Number of Booths |  |  |  | 1 |  | 
Category | Item | Cadence | Per Booth | Total Quantity | Supplier | Comments
Single Fill Items |  |  |  |  |  | 
Booth Screen | Front panel with clear screen and postbox (C) - W2m x H 2m | Single Fill | 1 | 1 | Speedy | 
Booth Screen | Side panel (B) - Screen W 2m x H 2m | Single Fill | 2 | 2 | Speedy | 
Booth Screen | 0.8m nib (D) - Screen W 0.8m x H 2m | Single Fill | 1 | 1 | Speedy | 
Infrastructure | Heras Fencing | Single Fill | N/A | As Required | Speedy | 
Infrastructure | Pedestrian Barrier | Single Fill | N/A | As Required | Speedy | 
Infrastructure | Tower Lighting | Single Fill | N/A | As Required | Speedy | 
Infrastructure | Traffic Management Signage | Single Fill | N/A | As Required | User | Responsibility of the user to provide
Infrastructure | Window opaque screen | Single Fill | N/A | As Required | Speedy | 
Infrastructure | Protective Flooring (Antinox/Buffalo, non-porous) | Single Fill | N/A | As Required | Speedy | Flooring will only be required where there is no non-porous alternative available, or where additional protection is mandated.
Cleaning | Biohazard Spill Kits | Single Fill and Replenishment | N/A | 6 | Speedy | For the disposal of human waste.
Cleaning | Cleaning Cloth - Blue | Single Fill and Replenishment | N/A | 12 | Speedy | 
Cleaning | Cleaning Cloth - Red | Single Fill and Replenishment | N/A | 12 | Speedy | 
Cleaning | Hand Sanitiser Pump Bottle (Booth and processor) - 500ML Refillable (min 70% alcohol content) | Single Fill | 2 | 2 | Speedy | As mandated in the Clinical SOP v2.4
Cleaning | Hand Sanitiser Pump Bottle (Other areas) - 500ML Refillable (min 70% alcohol content) | Single Fill | N/A | 4 | Speedy | 1x Collection, 1x Dropoff, 1x Don on/off, 1x Results reporter
Cleaning | Mop Bucket - Red | Single Fill | N/A | 1 | Speedy | 
Cleaning | Mop Bucket - Blue | Single Fill | N/A | 1 | Speedy | 
Cleaning | Mop Handle | Single Fill | N/A | 2 | Speedy | 
Cleaning | Sick Bowls - Disposable | Single Fill and Replenishment | N/A | 20 | Speedy | As mandated in the Clinical SOP v2.4
Cleaning | Squeegee | Single Fill and Replenishment | N/A | 1 | Speedy | Recommended item for efficiency in cleaning panelling or partition.
Cleaning | Wet floor signs | Single Fill | N/A | 4 | Speedy | 
Furniture | Processor Chair - plastic, non-porous, wipeable and can withstand chlorine solution | Single Fill | 1 | 1 | Speedy | 
Furniture | Staff Chair - plastic, non-porous, wipeable and can withstand chlorine solution | Single Fill | N/A | 5 | Speedy | 1x collection, 1x dropoff, 1x cleaner, 1x results, 1x spare (accesible)
Furniture | Processor Table (2m x 1m) - non-porous, wipeable and can withstand chlorine solution | Single Fill | 1 | 1 | Speedy | Please see Product Overview for specifications dependant on AT model.
Furniture | Staff Table (2m x 1m) - non-porous, wipeable and can withstand chlorine solution | Single Fill | N/A | 5 | Speedy | 1x Collection, 1x cleaning, 1x drop off, 1x don on/off, 1x results table
Printing | A2 Self Test Instruction Posters - Laminated | Single Fill | 1 | 1 | DHSC | 
Printing | ATS Signage pack - Laminated | Single Fill | N/A | 1 | DHSC | 
Staff | Digital Thermometer for Screening Staff | Single Fill | N/A | 2 | Speedy | Recommended item for best practice in ensuring staff are not displaying symptoms.
Stationery | Clock Batteries (sets) | Single Fill | N/A | 2 | Speedy | 
Stationery | Digital Clock | Single Fill | 1 | 1 | Speedy | Required for processing tables for noting time on LFD devices.
Stationery | Double Sided Tape - 50M | Single Fill | N/A | 1 | Speedy | Required to display the essential signage.
Stationery | Hazard Tape - 50M | Single Fill | N/A | 4 | Speedy | Required to mark out booth separation for staff and subjects.
Stationery | Plastic Crate - 35 Litre | Single Fill | N/A | 6 | Speedy | Recommended item for movement of PPE/test kits from the central secured stockroom.
Stationery | Plastic Wallets | Single Fill | N/A | 20 | Speedy | Recommended item for collation of invoices, incident reports, staff rota etc.
Stationery | Scissors | Single Fill | N/A | 1 | Speedy | 
Stationery | Wipeable Plastic Trays | Single Fill | 1 | 1 | Speedy | Required to move LFD devices between tables.
Stationery | Self Adhesive Coat Hooks | Single Fill | 1 | 1 | Speedy | 
Stationery | Self Adhesive Mirrors | Single Fill | 2 | 2 | Speedy | Required for subjects to locate the correct area to swab. 2 per booth to accommodate different heights
Waste | Clinical Waste Bins (booths and processor) | Single Fill | 2 | 2 | Speedy | 1x booth, 1x processor
Waste | Clinical Waste Bins (staff) | Single Fill | N/A | 2 | Speedy | 1x Results, 1x don on/off
Waste | Clinical Waste Mass Container (Large external) | Single Fill | N/A | 1 | User | Responsibility of the user to provide
Waste | Recycling Container (Large external) | Single Fill | N/A | 1 | User | Responsibility of the user to provide
Waste | Small General Waste Bin (Processors) | Single Fill | 1 | 1 | Speedy | 
Waste | Small General Waste Bin (Other areas) | Single Fill | N/A | 2 | Speedy | 1x don on/off, 1x collection
Waste | General Waste Mass Container (Large external) | Single Fill | N/A | 1 | User | Responsibility of the user to provide
Weekly Items |  |  |  |  |  | Adjust quantities accordingly due to actual usage
Cleaning | Chlorine Tablets | Weekly | N/A | 14 | Speedy | Required for mop and floor cleaning solution. Adjust quantity according to floor size. Alternative products available, please consult the Clinical SOP.
Cleaning | Mop Heads | Weekly | N/A | 2 | Speedy | 
Cleaning | Paper Towels | Weekly | N/A | 500 | Speedy | 
Cleaning | Hand Soap bottle with pump (500ml) | Weekly | N/A | 3 | Speedy | 
Cleaning | Selgiene Ultra 750 ml Bottle - Mixed | Weekly | N/A | 2 | Speedy | 
Cleaning | Boxes of Tissues - 100 Count | Weekly | N/A | 20 | Speedy | 
Cleaning | Hand Sanitiser - 5L | Weekly | N/A | 2 | Speedy | To refill the 500ml hand santiser pump bottles
Cleaning | Disinfectant Spray Bottle | Weekly | N/A | 2 | Speedy | 
Cleaning | Biodegradable Virucidal Wipes | Weekly | N/A | 200 | Speedy | Required for the cleaning and sanitising of devices on changeover and start/end of day.
Cleaning | Paper Towel Roll | Weekly | N/A | 2 | Speedy | 
Waste | Black Waste Binbags (rolls) | Weekly | N/A | 3 | Speedy | 
Waste | Orange Clinical Waste Binbags (rolls) | Weekly | N/A | 5 | Speedy | 
Waste | Yellow Biowaste Seal Tags | Weekly | N/A | 100 | Speedy | 

## Slide 67: OPTION B: BILL OF MATERIALS FOR SINGLE OR MULTI OPEN PLAN LAYOUT
Single or Multi Open Plan Layout - Bill of Materials Please note distinction between Single Fill and Weekly level items. Replenishment items are expected to deteriorate over time and as such should be replaced as requried, but on no fixed cadence. |  |  |  |  |  | 
Key: User = customer e.g. University SOP = Standard Operating Procedure |  |  |  |  |  | 
Number of Booths |  |  |  | 1 |  | 
Category | Item | Cadence | Per Booth | Total Quantity | Supplier | Comments
Single Fill Items |  |  |  |  |  | 
Booth Screen | Acrylic protective clear screen - W 0.76m x H 0.796m | Single Fill | 1 | 1 | Speedy | 
Infrastructure | Heras Fencing | Single Fill | N/A | As Required | Speedy | 
Infrastructure | Pedestrian Barrier | Single Fill | N/A | As Required | Speedy | 
Infrastructure | Tower Lighting | Single Fill | N/A | As Required | Speedy | 
Infrastructure | Traffic Management Signage | Single Fill | N/A | As Required | User | Responsibility of the user to provide
Infrastructure | Window opaque screen | Single Fill | N/A | As Required | Speedy | 
Infrastructure | Protective Flooring (Antinox/Buffalo, non-porous) | Single Fill | N/A | As Required | Speedy | Flooring will only be required where there is no non-porous alternative available, or where additional protection is mandated.
Infrastructure | Partition | Single Fill | 2 | 2 | Speedy | Optional Partition that allows for reduction of distancing between stations
Cleaning | Biohazard Spill Kits | Single Fill and Replenishment | N/A | 6 | Speedy | For the disposal of human waste.
Cleaning | Cleaning Cloth - Blue | Single Fill and Replenishment | N/A | 12 | Speedy | 
Cleaning | Cleaning Cloth - Red | Single Fill and Replenishment | N/A | 12 | Speedy | 
Cleaning | Hand Sanitiser Pump Bottle (Booth and processor) - 500ML Refillable (min 70% alcohol content) | Single Fill | 2 | 2 | Speedy | As mandated in the Clinical SOP v2.4
Cleaning | Hand Sanitiser Pump Bottle (Other areas) - 500ML Refillable (min 70% alcohol content) | Single Fill | N/A | 4 | Speedy | 1x Collection, 1x Dropoff, 1x Don on/off, 1x Results reporter (if 3+ testing booths then formula will add an extra for a second results reporter)
Cleaning | Mop Bucket - Red | Single Fill | N/A | 1 | Speedy | 
Cleaning | Mop Bucket - Blue | Single Fill | N/A | 1 | Speedy | 
Cleaning | Mop Handle | Single Fill | N/A | 2 | Speedy | 
Cleaning | Sick Bowls - Disposable | Single Fill and Replenishment | N/A | 20 | Speedy | As mandated in the Clinical SOP v2.4
Cleaning | Squeegee | Single Fill and Replenishment | N/A | 1 | Speedy | Recommended item for efficiency in cleaning panelling or partition.
Cleaning | Wet floor signs | Single Fill | N/A | 4 | Speedy | 
Furniture | Booth Chair - plastic, non-porous, wipeable and can withstand chlorine solution | Single Fill | 2 | 2 | Speedy | 
Furniture | Staff Chair - plastic, non-porous, wipeable and can withstand chlorine solution | Single Fill | N/A | 5 | Speedy | 1x collection, 1x dropoff, 1x cleaner, 1x results (2x if 3+ test booths), 1x spare (accesible)
Furniture | Processor Table (1m x 1m) - non-porous, wipeable and can withstand chlorine solution | Single Fill | 1 | 1 | Speedy | Please see Product Overview for specifications dependant on AT model.
Furniture | Staff Table (2m x 1m) - non-porous, wipeable and can withstand chlorine solution | Single Fill | N/A | 5 | Speedy | 1x Collection, 1x cleaning, 1x drop off, 1x don on/off, 1x results table (2x if 3+test booths)
Printing | A2 Self Test Instruction Posters - Laminated | Single Fill | 1 | 1 | DHSC | 
Printing | ATS Signage pack - Laminated | Single Fill | N/A | 1 | DHSC | 
Staff | Digital Thermometer for Screening Staff | Single Fill | N/A | 2 | Speedy | Recommended item for best practice in ensuring staff are not displaying symptoms.
Stationery | Clock Batteries (sets) | Single Fill | N/A | 2 | Speedy | 
Stationery | Digital Clock | Single Fill | 1 | 1 | Speedy | Required for processing tables for noting time on LFD devices.
Stationery | Double Sided Tape - 50M | Single Fill | N/A | 1 | Speedy | Required to display the essential signage.
Stationery | Hazard Tape - 50M | Single Fill | N/A | 4 | Speedy | Required to mark out booth separation for staff and subjects.
Stationery | Plastic Crate - 35 Litre | Single Fill | N/A | 6 | Speedy | Recommended item for movement of PPE/test kits from the central secured stockroom.
Stationery | Plastic Wallets | Single Fill | N/A | 20 | Speedy | Recommended item for collation of invoices, incident reports, staff rota etc.
Stationery | Scissors | Single Fill | N/A | 1 | Speedy | 
Stationery | Wipeable Plastic Trays | Single Fill | 1 | 1 | Speedy | Required to move LFD devices between tables.
Stationery | Self Adhesive Coat Hooks | Single Fill | 1 | 1 | Speedy | 
Stationery | Self Adhesive Mirrors | Single Fill | 2 | 2 | Speedy | Required for subjects to locate the correct area to swab. 2 per booth to accommodate different heights
Waste | Clinical Waste Bins (booths and processor) | Single Fill | 2 | 2 | Speedy | 1x booth, 1x processor
Waste | Clinical Waste Bins (staff) | Single Fill | N/A | 2 | Speedy | 1x Results (2x if 3+ test booths), 1x don on/off
Waste | Clinical Waste Mass Container (Large external) | Single Fill | N/A | 1 | User | Responsibility of the user to provide
Waste | Recycling Container (Large external) | Single Fill | N/A | 1 | User | Responsibility of the user to provide
Waste | Small General Waste Bin (Processors) | Single Fill | 1 | 1 | Speedy | 
Waste | Small General Waste Bin (Other areas) | Single Fill | N/A | 2 | Speedy | 1x don on/off, 1x collection
Waste | General Waste Mass Container (Large external) | Single Fill | N/A | 1 | User | Responsibility of the user to provide
Weekly Items |  |  |  |  |  | Adjust quantities accordingly due to actual usage
Cleaning | Chlorine Tablets | Weekly | N/A | 14 | Speedy | Required for mop and floor cleaning solution. Adjust quantity according to floor size. Alternative products available, please consult the Clinical SOP.
Cleaning | Mop Heads | Weekly | N/A | 2 | Speedy | 
Cleaning | Paper Towels | Weekly | N/A | 500 | Speedy | 
Cleaning | Hand Soap bottle with pump (500ml) | Weekly | N/A | 3 | Speedy | 
Cleaning | Selgiene Ultra 750 ml Bottle - Mixed | Weekly | N/A | 2 | Speedy | 
Cleaning | Boxes of Tissues - 100 Count | Weekly | N/A | 20 | Speedy | 
Cleaning | Hand Sanitiser - 5L | Weekly | N/A | 2 | Speedy | To refill the 500ml hand santiser pump bottles
Cleaning | Disinfectant Spray Bottle | Weekly | N/A | 2 | Speedy | 
Cleaning | Paper Towel Roll | Weekly | N/A | 2 | Speedy | 
Cleaning | Biodegradable Virucidal Wipes | Weekly | N/A | 200 | Speedy | Required for the cleaning and sanitising of devices on changeover and start/end of day.
Waste | Black Waste Binbags (rolls) | Weekly | N/A | 3 | Speedy | 
Waste | Orange Clinical Waste Binbags (rolls) | Weekly | N/A | 5 | Speedy | 
Waste | Yellow Biowaste Seal Tags | Weekly | N/A | 100 | Speedy | 

## Slide 68: SOURCING MATERIALS
PROCESS FOR ORDERING:
Complete the ”Bill of Materials” spreadsheet and send with contact details to covidsupplies@speedyservices.com
Speedy will contact you to confirm the equipment items, prices and quantities with you and will also arrange payment and equipment delivery
SPEEDY DEDICATED SUPPLY SUPPORT TEAM:
01332 850 004 (Option 4)
covidsupplies@speedyservices.com
ESCALATION CONTACTS:
James O’Sullivan - Account Manager james.osullivan1@speedyservices.com 07515 052 260
Jeremy Jowett - Commercial Director jeremy.jowett@speedyservices.com
Speedy are an approved supplier to purchase the clinically approved equipment on the Bill of Materials to set up Asymptomatic Testing sites.

## Slide 69: 3.7 PERMANENT SITE CLOSURE GUIDELINES

## Slide 70: GENERAL CONSIDERATIONS
The following provides the recommended guidelines for closure of asymptomatic testing sites (ATS). The contents were accurate at the time of publication, however, are subject to change based on learning from testing sites and policies of the National Testing Programme. This is not considered to be final and must be considered with the latest clinical guidance.
CLEANING/INFECTION CONTROL
All materials must be sufficiently cleaned to adhere to the clinical SOP for decontamination.
HEALTH CARE WASTE
All health care waste to be disposed of according to the latest waste guidance in the Master Clinical SOP.
CLOSURE DATE
Leave a minimum of 5 days’ lead time to inform all relevant groups (internally and externally) to prepare and decommission the site*, including mobilising appropriate logistics required for storage, waste or recycling
*Extensions to closure date – inform all relevant parties regarding digital, logistics and suppliers. Check stock levels and contact relevant supply channels for further supplies to meet the extended run phase.
INVENTORY
All infrastructure and re-usable items to be included in a closure condition report, clearly identifying when items would not be fit for re-use. Remaining fit-for-purpose items can be stored and re-used if clinical cleaning and decontamination protocols are adhered to.
SITE LEASE / USAGE AGREEMENT
Refer to any site lease, usage agreement (or other formal agreement) that acknowledges the responsibilities of the customer and ensure there are no outstanding or pending liabilities ahead of handing back to the site owner.

## Slide 71: OTHER CONSIDERATIONS
INFRASTRUCTURE:
Infrastructure constitutes, but is not limited to; Partitions, Perspex screens, flooring, tables and chairs. Please check the associated BOM specific to your site model specifications to accurately cross reference.
All infrastructure must be cleaned, in-line with the clinical guidelines, in-situ ahead of dismantlement. All infrastructure items must then be carefully dismantled, stacked and stored in a clean environment that permits re-use.
It is recommended that any items that are no longer of use to the user should be recycled or disposed of responsibly.
GENERAL SUPPLIES:
All other items that are not PPE, Kits, devices and infrastructure can be kept, re-used in-line with clinical decontamination guidelines or recycled.
TESTS AND PPE:
Provide an inventory of remaining test kits (incl. type(s)), barcodes and PPE. Ensure and confirm that tests are, and have been, stored throughout within the temperature dependency limits so that they may be re-distributed and are fit for future purpose.
5 days’ lead time to contact and arrange for collection of test devices and PPE with the supply team.
DIGITAL:
Refer to the "Managed devices" section in the digital guidebook for instructions on arranging pickup of managed devices.

## Slide 72: 4 WORKFORCE
VERSION 2.5
Roles, positions, and responsibilities
Workforce considerations
Workforce blueprint & calculator
Workforce training

## Slide 73: 4.1 ROLES, POSITIONS AND RESPONSIBILITIES

## Slide 74: CORE ROLES
ROLE | KEY RESPONSIBILITIES
Team Leader | Responsible for the overall on-site operations at the testing site, including day-to-day workforce management. Several Supervisor or Deputy Team Leader roles may be needed for larger sites – this should be designed at a site level. It is advised the span of control does not exceed 15 people on per supervisor role.
Site Operative | Helping manage the site and supporting Participants through the testing process. From queue management, to registration and supporting testing. The role has three positions: Queue Coordinator, Registration Assistant, and Test Assistant.
Testing Operative | Conducting the processing and analysis of tests to ensure the process is conducted accurately and uploaded to the system. The role has two positions: Processing Operative, and Results Recorder. Results will be passed on to existing Local Contact Tracers or coordinated with the national programme.
These roles represent the jobs that people will arrive at sites having been brought in for. The next 3 slides explain the position that people within these roles are then expected to be trained in. It is presumed that each person within a role will be able to fill in any of the positions but will be expected to carry out one position at any given time. Full job descriptions can be found in the appendix
ROLES, POSITIONS AND RESPONSIBILITIES:

## Slide 75: TEAM LEADER
STAFF POSITION | KEY RESPONSIBILITIES
Team Leader Several Supervisor or Deputy Team Leader roles may be needed for larger sites – this should be designed at a site level. It is advised the span of control does not exceed 15 people on per supervisor role | Responsible for the overall on-site operations at the testing site, including day-to-day workforce management Running day-to-day operations including adverse incident reporting, on-site workforce management, managing site health & safety and receiving and managing stock Point of escalation for any issues on site, and escalates to local public health officials as appropriate Ensure adherence to SOP and clinical guidance is maintained throughout operations Responsible for safety and security of the site If Participants raise any data privacy concerns, directs Participants to the Data Privacy Notice which explains how we will use their data (https://www.gov.uk/government/publications/coronavirus-covid-19-testing-privacy-information) Responsibility for the quality and risk management of the testing and regularly checking that the site meets the standards required
Roles, positions and responsibilities may need to be adapted on a site-by-site basis depending on the size and target throughput of your testing sites. Roles and positions can be performed by the same person (if appropriate).
ROLES, POSITIONS AND RESPONSIBILITIES:

## Slide 76: SITE OPERATIVE
STAFF POSITIONS | KEY RESPONSIBILITIES
Queue Coordinator | Ensures orderly entry of Participants onto the testing site. Ensures crowd control and social distancing is maintained in Participant queueing areas Monitor Participants in the queue who are showing symptoms of COVID and acts accordingly if they are In case of long queue, encourages people in line to start registering online Supports general site set up, including appropriate signage to manage Participant flow
Registration Assistant | Responsible for ensuring Participants have registered and are eligible for testing. Greets Participant at arrival, asks them to sanitise hands and ensures the Participant is eligible for asymptomatic testing Aids the Participant in registering for the test if they are unable to Provides assistance for people who might not have the relevant digital information such as phone number and email address Guides people who are coming and for a valid reason need to test anonymously ‘Drip feeds’ Participants into testing area, ensuring testing area does not exceed maximum capacity Communicate to test Participants the purpose of participating in testing at your site and the testing journey.
Test Assistant | Provides guidance to Participants on swabbing as requested and ensures cleaning of booths. Directs Participant to available testing stations and directs them to the exit when they are finished On hand to provide Participant with additional verbal instructions if required Provides regular cleaning to testing stations throughout day (Participants are also ask to self-clean between each test)
Roles, positions and responsibilities may need to be adapted on a site by site basis depending on the size and target throughput of your testing sites. Roles and positions can be performed by the same person (if appropriate).
ROLES, POSITIONS AND RESPONSIBILITIES:

## Slide 77: TESTING OPERATIVE
STAFF POSITIONS | KEY RESPONSIBILITIES
Processing Operative | Prepares test sample for analysis and interprets result. Sets up sample for analysis, and pipettes reagent to sample Times the sample analysis Await and read result displayed, and mark it on device* Provides to Results Recorder to upload to digital platform *At most sites, the Processing operative will oversee around 4 to 6 LFDs developing at any one time
Results Recorder | Collates results from Processing Operatives and uploads to digital solution. Reads test result outcome (marked by Processing Operative) Enters result onto a managed device, including scan of QR code (result is automatically sent to Test & Trace)
Roles, positions and responsibilities may need to be adapted on a site by site basis depending on the size and target throughput of your testing sites. Roles and positions can be performed by the same person (if appropriate).
ROLES, POSITIONS AND RESPONSIBILITIES:

## Slide 78: PPE REQUIREMENTS
PPE should be changed whenever staff members leave and re-enter the testing site area (per session) or if protective properties are compromised or contaminated.
Processing Operatives must change gloves between samples.
Position | Disposable gloves | Disposable plastic apron | Fluid-resistant (Type 11R) surgical mask (FRSM) | Eye protection (Goggles or visor)
Registration Assistant | × | × | P | ×
Test Assistant | × | × | P | ×
Processing Operative | P | P | P | P
Results Recorder | × | × | P | ×
Queue Coordinator | × | × | P | ×
ROLES, POSITIONS AND RESPONSIBILITIES:

## Slide 79: 4.2 WORKFORCE CONSIDERATIONS

## Slide 80: GENERAL
There are general consideration that should be made for the site
Staff should disable the Test & Trace app when working on the testing site.
There is no requirement for staff to have DBS checks as long as in settings where ones are required (Social Care, Schools) relevant people from the organisation are there to ensure safeguarding
There will be no reporting facility for sites to extract training data for privacy reasons. Instead, staff can take a screenshot upon completing/passing the assessment as proof of training completion.
For staff onsite it is a suggested that they are marked as staff using badges or hi-vis but this is at the discretion of the site to work out how best to show someone is staff in the context of the site and if it is needed
CONSIDERATIONS:

## Slide 81: SUPPORTING TEST PARTICIPANTS WITH ACCESS NEEDS
STAFFING CONSIDERATIONS:
Skillset
For recruitment we suggest ideally aiming to recruit staff who speak multiple languages, especially the languages predominant in the locality
Attire
A visual indicator (e.g. badge, sticker) of additional languages spoken
Appropriate Personal Protective Equipment﻿ (PPE)
Mindset
Staff should consider the following when interacting with individuals, who may have physical, sensory or cognitive disabilities:
To offer assistance when someone appears lost or confused or where people clearly have a disability or indicate that they have a hidden one
Find out what assistance they need and avoid rushing them through the process
Training
Staff should know how to support people with language / communication barriers
They should also be trained to support non-digital customers through the journey
More information on the varied needs of users is available on the following slides
OFFICIAL SENSITIVE – DO NOT SHARE FURTHER WITHOUT PERMISSION – SUBJECT TO LEGAL, REGULATORY AND POLICY REVIEW
CONSIDERATIONS:

## Slide 82: SUPPORTING BLIND & PARTIALLY SIGHTED TEST PARTICIPANTS
SUPPORTING BLIND OR PARTIALLY SIGHTED PEOPLE:
Tips to help communicate with a person with sight loss who attends an ATS:
Gain the person’s attention by speaking to them
Introduce yourself and what you do
Always talk to the person directly, rather than their sighted companion
Use verbal responses, avoid nods and head shakes
Verbalise your actions
Inform people when you are walking away from them or leaving the room
Remember if someone is blind, it doesn’t always mean they have no sight at all
In a group conversation, always make it clear who you are and who you are speaking to
Provide information in an alternative/accessible way such as digital, audio, large print or braille
If someone is struggling with the self-test and has attended with a companion carer, friend or family member, if the user would prefer this and the companion is happy to do so, allow the companion to ‘self-test’ the user
FURTHER INFORMATION
michael.wordingham@rnib.org.uk
mike.bell@pocklington-trust.org.uk
A blanket, one-size-fits-all approach will not work for all people with additional accessibility requirements. This page outlines some measures which could be helpful for specific groups. Please always consider the needs of individuals on a case by case basis.
CONSIDERATIONS:

## Slide 83: SUPPORTING EMPLOYEES WITH HIDDEN DISABILITIES
A blanket, one-size-fits-all approach will not work for all people with additional accessibility requirements. This page outlines some measures which could be helpful for specific groups. Please always consider the needs of individuals on a case by case basis.
CONSIDERATIONS:
SOCIAL DISTANCING WEARABLES
Disabled people, people with sight loss, older people and people with mobility issues may find social distancing challenging. It is not always easy to identify such individuals, however, there are a number of wearable products that people may use to indicate to others that they want to maintain their distance but find this difficult. Further info from: https://pleasegivemespace.uk/ and https://www.bevancommission.org/distance-aware
HIDDEN DISABILITIES
These are generally not identifiable, however some people with hidden disabilities may display a sun flower lanyard.

## Slide 84: SUPPORTING EMPLOYEES WITH OTHER NEEDS
PEOPLE WITH AUTISM:
Some people with autism may struggle with the self-swabbing. A potential solution would be to allow the user’s carer to swab’ the individual.
PEOPLE WITH ANXIETY:
Some people may get anxious at the testing site. In these circumstances, please allow the person to wait until they feel more settled, and/or to recover in a private area.
PEOPLE WITH LEARNING DISABILITIES:
Some people, who are unable to ‘self-test’ themselves may prefer their carer or someone who they know to ‘self-test’ them rather than a tester who they do not know.
LANGUAGE BARRIERS:
Ensure you have accessible testing instructions in a range of languages and formats, including easy-read and British Sign Language and braille.
DIGITIALLY EXCLUDED:
People who lack digital skills or who do not have a smartphone / email address will need a tailored service. For more information, please go to the ‘Testing for non-digital participants’ section on page 152.
FACE MASK EXEMPTION:
In many UK public settings some people may be exempt from wearing a face covering e.g. if they have sight loss or specific health conditions. They may carry a card, badge or wear a Sunflower lanyard to signal a hidden disability. This is a personal choice and is not required by law https://hiddendisabilitiesstore.com/.
The Standard Operating Procedures (SOP) for Local Testing Sites and Mobile Testing Units state that the only exemption from wearing a face covering is for children aged under 3. This clinical policy is in place to minimise the risk of passing on the virus in (typically indoor) settings where symptomatic people may be present.
CONSIDERATIONS:
A blanket, one-size-fits-all approach will not work for all people with additional accessibility requirements. This page outlines some measures which could be helpful for specific groups. Please always consider the needs of individuals on a case by case basis.

## Slide 85: 4.3 WORKFORCE BLUEPRINT & CALCULATOR

## Slide 86: USING THE WORKFORCE BLUEPRINT
UTILISE THE WORKFORCE BLUEPRINT BY:
Understanding the daily testing demand and testing site capacity targets over time
The main blueprints and ratios are based on a 100% capacity site (10 per hour, per bay). We expect the ratios and total FTE to be reduced at sites expecting lower throughput. Tables showing these have been included in the appendix and the accompanying excel can have different capacities.
Identifying the workforce requirement for a single ATS by:
  Identifying an ATS archetype of a similar size and use the workforce blueprint to understand resourcing requirements; OR
  Input the desired ATS variables (size and throughput) in the calculator to understand the workforce requirement
  The workforce blueprint and calculator give static numbers required to operate all positions at a given time. Consider whether an uplift in numbers is needed to cover breaks and absences (c. 15% recommended)
Multiplying the workforce requirement for a single ATS by the total number of ATS over time
Review the workforce numbers and localise to accommodate any setting specific requirements
The workforce blueprints are designed to complement any ATS SOPs or operating manuals. They also act as a guide to identify the workforce requirements and numbers. Sourcing, training and wider end-to-end workforce management (e.g. payroll) will also need to be considered.
WORKFORCE BLUEPRINT & CALCULATOR:

## Slide 87: SMALL ATS 100% THROUGHPUT
Role Adaptation 1 - Registration Assistant: On this smaller scale site, registration assistant and test assistant have been combined as one front of house role
Role Adaptation 2 – Results Recorder: The results recording can then be done by the processing operative and/or the site lead which some testing sites have done to help with the process flow
Roles provided above are static workforce numbers required to operate all positions at any given time. It is recommended that staff rotate across multiple positions throughout the day, with breaks staggered to ensure no disruption to operations whilst providing all staff equal break time.
SIZE OF ATS | Small (1 Testing Station)
DAILY CAPACITY | 80
THROUGHPUT | Maximum (100%)
STATIC WORKFORCE FTE | 3
WORKFORCE BLUEPRINT & CALCULATOR:
Testing Operative
Site Operative
Key
Team Leader
Site Management
Team Leader
(1 FTE)
Registration & Testing Coordination
Registration Assistant /Test Assistant
(1 FTE)
Sample Analysis
Processing Operative/Results Recorder
(1 FTE)

## Slide 88: MEDIUM ATS 100% THROUGHPUT
Role Adaptation - Queue Coordinator: At this scale of site a queue coordinator is not specified, however if queues need to be managed and this would be done by the registration assistant and test assistant depending on where the queues formed on the site.
Roles provided above are static workforce numbers required to operate all positions at any given time. A 15% uplift in workforce is recommended to cover staff breaks and absences. It is recommended that staff rotate across multiple positions throughout the day, with breaks staggered to ensure no disruption to operations whilst providing all staff equal break time. To alter this view for capacities other than 100% please see the supporting excel calculator or see appendix to this PPT.
SIZE OF ATS | Medium (6 Testing Stations)
DAILY CAPACITY | 480
THROUGHPUT | Maximum (100%)
STATIC WORKFORCE FTE | 12 (+2 break/absence cover)
Testing Operative
Site Operative
Key
Team Leader
Site Management
Team Leader
(1 FTE)
Sample Analysis
Results Recorder (2 FTE)
Processing Operative (6 FTE)
Registration & Testing Coordination
Test Assistant (2 FTE)
Registration Assistant (1 FTE)
WORKFORCE BLUEPRINT & MODEL:

## Slide 89: LARGE ATS 100% THROUGHPUT
Role provided above are static workforce numbers required to operate all positions at any given time. A 15% uplift in workforce is recommended to cover staff breaks and absences. It is recommended that staff rotate across multiple positions throughout the day, with breaks staggered to ensure no disruption to operations whilst providing all staff equal break time. To alter this view for capacities other than 100% please see the supporting excel calculator or see appendix to this PPT.
Testing Operative
Site Operative
Key
Team Leader
Site Management
Team Leader
(1 FTE)
Queue Support
Queue Coordinator
(3 FTE*)
Registration & Testing Coordination
Registration Assistant (5 FTE)
Test Assistant (6 FTE)
Sample Analysis
Results Recorder (5 FTE)
Processing Operative (24 FTE)
SIZE OF ATS | Large (24 Testing Stations)
DAILY CAPACITY | 1920
THROUGHPUT | Maximum (100%)
STATIC WORKFORCE FTE | 44 (+7 break/absence cover)
WORKFORCE BLUEPRINT & MODEL:

## Slide 90: WORKFORCE BLUEPRINT ASSUMPTIONS
This calculator is based on a number of assumptions:
Ratios and FTE counts based off of 100% capacity, reduction will be made for lower throughput
Assumes the Innova SARS-Cov-2 Antigen Test Devices in use at ATS only. Further iterations will baseline against future technologies
Assumes that self-swab only at the ATS, with samples always processed by dedicated resource (non-Participant sample processing)
Does not consider infrastructure or real estate constraints, including those needed to accommodate social distancing
Assumes that sufficient measures are taken to ensure the ATS is not clinically classified as a lab, which would therefore entail additional workforce requirements
Does not include specific ancillary roles, such as security etc
Assumes the sample must rest for at least twenty minutes before analysis
As more testing sites are delivered we expect the calculators and number to iterate in response to lessons learned.
All ratios are based on maximum site capacity (10 tests per test station per hour). Should throughput be lower than this, workforce should be reduced – see workforce calculator for guidance.
Workforce should be flexibly resources across positions depending on site by site requirements. The above is indicative guidance to support calculating workforce, but is not a definitive allocation of resource for every site. Team Leaders should make management decisions on site to ensure adequate resource are position across the testing site.
WORKFORCE BLUEPRINT & CALCULATOR:

## Slide 91
WORKFORCE POSITION VALIDATION FROM PILOTS
ROLE | FTE | RATIONALE | VALIDATION AND FEEDBACK | PILOT FEEDBACK LOCATIONS
Team Leader | 1 FTE per site | A leadership role needed on all sites for smooth operations. However, role can be combined with Results Recorder for small sites | - | -
Queue Coordinator | 1 FTE per 600 daily capacity | Assumed estimate based on average throughput per hour. Appropriate number likely to be influenced on site infrastructure. | Queue can become long and management of them in needed Pre existing queuing infrastructure can be used The queues for sites can often stretch into areas not in the site limits so need management | Liverpool
Registration Assistant | 1 FTE per 5 Testing Stations | Based on numbers currently in operation at existing testing sites. Assumes a moderate number of Participants need registration support. | On the ground feedback that the process often requires guidance from staff The expectation that not all Participants will come with a device capable of registration Guidance can be given to multiple Participants at once | JLP/ Liverpool/ DMU
Test Assistant | 1 FTE per 4 Testing Stations | Based on numbers used for early ATS pilots, including Liverpool mass testing. Assumes sporadic cleaning to test booths (due to self-clean). | Participants sometimes need help with the test in the booths There is a need to coordinate people entering the booths Requirement to observe when deep cleans need to happen in bays from possible bodily fluid transfers | Liverpool/ DMU
Processing Operative | 1 FTE per 1 Testing Stations | Conservative estimate on number of individuals need to for sample analysis. Assumes 6 minutes per test for operative to prepare and read sample. | The job requires focus and multiple steps so focusing on one test at a time is preferred Often gives guidance to the Participant, especially when the bays have Perspex May be flexed with Results Recorder position should task delineation change | Liverpool/ DMU
Results Recorder | 1 FTE per 5 Testing Stations | Based on learnings from pilots and current workforce allocation at pilots. Should task delineation with Processing Operative be adjusted, workforce may need to be flexed across these roles (see note below) | The process of recording can be quick but more time is allocated to make sure results are accurate The role is limited by the devices on site | Liverpool/ DMU
A key consideration when defining the specific roles and numbers, of workforce for an individual testing site is the ratio of certain roles to testing stations. Based on several pilots, below is a guide to the ratio’s to consider for a site with 100% capacity testing demand and a medium to large site.
Consideration 1: There are other roles a site might want to consider e.g. Cleaners, supply, security, assisted, etc. that organisations might want to consider when planning workforce
Consideration 2: When capacity is reduced the calculator reduces the FTE requirement by the same percentage up until it gets to the minimum staff of Team Lead, Test Assistant and Processing Ops, as seen on the 1 booth calculator
WORKFORCE BLUEPRINT & CALCULATOR:

## Slide 92
 |  | Number of Testing Stations (Testing Site Size) |  |  |  |  |  |  |  |  |  |  |  |  | 
Role | Position | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14
Team Leader |  | 1* | 1* | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
Site Operations Role | Queue Coordinator** | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 2 | 2 | 2
 | Registration Assistant | 0 | 0 | 1 | 1 | 1 | 1 | 1 | 2 | 2 | 2 | 2 | 2 | 3 | 3
 | Test Assistant*** | 1 | 1 | 1 | 1 | 1 | 2 | 2 | 2 | 2 | 3 | 3 | 3 | 3 | 4
Testing Operations Role | Processing Operative | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14
 | Results Recorder | 0 | 0 | 0 | 1 | 1 | 2 | 2 | 2 | 2 | 2 | 3 | 3 | 3 | 3
Break & Absence Cover (8 hrs operations) |  | 0 | 1 | 1 | 1 | 1 | 2 | 2 | 2 | 3 | 3 | 3 | 3 | 4 | 4
Total (8 hrs operations) |  | 3 | 5 | 7 | 9 | 10 | 14 | 15 | 18 | 20 | 22 | 24 | 26 | 29 | 31
Daily Capacity (8hr operations) |  | 80 | 160 | 240 | 320 | 400 | 480 | 560 | 640 | 720 | 800 | 880 | 960 | 1040 | 1120
Team Leader to cover as Results Recorder for small sites
** Queue Coordinator requirements are particularly indicative and should be determined on a site by site basis, dependent on site specific requirements and local infrastructure
Note: Assumes all Participants to use self-swab. For minors and those unable to self-swab, assumes a guardian or career will assist with swabbing
Note: Assumes sufficient workforce to deliver maximum potential capacity (1 test every 6 minutes per testing station)
Note: Additional contingency resource has been added to cover breaks and potential absences. It is recommended that staff rotate across multiple positions throughout the day, with breaks and all staff provided equal break time
WORKFORCE RESOURCE REQUIREMENTS PER 100% CAPACITY TESTING SITE SIZE (1/2)
The table below outlines the indicative number of staff needed to operate a testing site per shift to maximum capacity, there is further slides in the appendix showing a medium and low capacity.
This is based off an 8 hour day and a 10 throughput per testing station per hour
Additional contingency resource has been added to cover breaks and potential absences. It is recommended that staff rotate across multiple positions throughout the day, with breaks and all staff provided equal break time
Workforce numbers are a guideline only and local decisions should be made on a sensible workforce size on a site by site basis.
WORKFORCE BLUEPRINT & CALCULATOR:

## Slide 93
 |  | Number of Testing Stations (Testing Site Size) |  |  |  |  |  |  |  |  |  |  |  |  | 
Role | Position | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28
Team Leader |  | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
Site Operations Role | Queue Coordinator** | 2 | 2 | 2 | 2 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 4 | 4
 | Registration Assistant | 3 | 3 | 3 | 4 | 4 | 4 | 4 | 4 | 5 | 5 | 5 | 5 | 5 | 6
 | Test Assistant*** | 4 | 4 | 4 | 5 | 5 | 5 | 5 | 6 | 6 | 6 | 6 | 7 | 7 | 7
Testing Operations Role | Processing Operative | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28
 | Results Recorder | 3 | 4 | 4 | 4 | 4 | 4 | 5 | 5 | 5 | 5 | 5 | 6 | 6 | 6
Break & Absence Cover (8 hrs operations) |  | 4 | 5 | 5 | 5 | 5 | 6 | 6 | 6 | 6 | 7 | 7 | 7 | 8 | 8
Total (8 hrs operations) |  | 32 | 35 | 36 | 39 | 41 | 43 | 45 | 47 | 49 | 51 | 52 | 55 | 58 | 60
Daily Capacity (8hr operations) |  | 1200 | 1280 | 1360 | 1440 | 1520 | 1600 | 1680 | 1760 | 1840 | 1920 | 2000 | 2080 | 2160 | 2240
WORKFORCE RESOURCE REQUIREMENTS PER 100% CAPACITY TESTING SITE SIZE (2/2)
Team Leader to cover as Results Recorder for small sites
** Queue Coordinator requirements are particularly indicative and should be determined on a site by site basis, dependent on site specific requirements and local infrastructure
Note: Assumes all Participants to use self-swab. For minors and those unable to self-swab, assumes a guardian or career will assist with swabbing
Note: Assumes sufficient workforce to deliver maximum potential capacity (1 test every 6 minutes per testing station)
Note: Additional contingency resource has been added to cover breaks and potential absences. It is recommended that staff rotate across multiple positions throughout the day, with breaks and all staff provided equal break time
The table below outlines the indicative number of staff needed to operate a testing site per shift to maximum capacity, there is further slides in the appendix showing a medium and low capacity.
This is based off an 8 hour day and a 10 throughput per testing station per hour
Additional contingency resource has been added to cover breaks and potential absences. It is recommended that staff rotate across multiple positions throughout the day, with breaks and all staff provided equal break time
Workforce numbers are a guideline only and local decisions should be made on a sensible workforce size on a site by site basis.
WORKFORCE BLUEPRINT & CALCULATOR:

## Slide 94: 4.4 WORKFORCE TRAINING

## Slide 95: TRAINING OVERVIEW
1
3
4
5
END TO END PROCESS:
Take your test staff site through the end to end testing process
PRACTICE:
After completing the online training for test processing, trainees are encouraged to practice using the testing device by swabbing themselves and processing the results.
DRESS REHEARSAL:
Take your testing site staff to your testing site and run a series of “dress rehearsals” to simulate what they will experience when they start testing your Employees. This will help your testing site staff to put in practice everything they have learned so far. Use role play to pretend to be Employees getting tested.
“WHAT IF” SCENARIOS:
Take your dress rehearsals to the extreme by simulating situations that your testing site staff may experience, for example, what if:
someone becomes physically ill in the test booth?
someone receives a positive notification on the testing site, and needs support?
someone is feeling highly anxious about the testing process, and needs support?
someone needs support to fill in their digital registration form?
a test kit becomes contaminated (e.g. someone drops their swab?)
Organisations should dedicate a full day to train your testing site staff and should take place either in a classroom setting or at your physical testing site. Organisations should train their testing site staff a few days before they start testing their participants as this will give them time to familiarise themselves with their roles and responsibilities.
For questions specifically about training content, email
testertraining@dhsc.gov.uk
For technical queries about the training platform contact 0161 903 1032 (Mon-Fri 8:30-18:00, Sat-Sun 10:00-16:00, including bank holidays)
2
ONLINE TRAINING:
Staff will need to complete the relevant online training modules relevant to their roles and responsibilities. They will also be required to complete an online assessment and read the guidance materials in the Resources section

## Slide 96: ONLINE TRAINING PLATFORM
OVERVIEW:
The online training platform is tailored for workforces who are running asymptomatic testing sites using “Innova Lateral Flow Technology test kits” (additional training will become available when other test kits become available)
Testing site workforce will have access to a selection of online modules and assessments, testing site staff will need to review the content of these modules and complete the assessments
Testing site staff should complete their online training before they start practical training

## Slide 97: ONLINE TRAINING MODULES
Module | Topics
Module 1: LFD Process | Checking you’re using the right device Checks before you start A step-by-step process on how to use the device Reading the result Marking the device with the result FAQ’s
Module 2: LFD results recording | Inputting a positive, negative or void result into the recording application How the Participant’s testing data is used in the T&T system
Module 3: PPE and Infection Control | PPE donning and doffing PPE adjustments Infection prevention measures Hygiene and cleanliness
Module 4: Guiding the Participant through swabbing | Verbal support Instructions for the Participant Handling Participant concerns Options when nasal and throat swabs become infeasible
Module 5: Meet and Greet | Greeting the Participant at the entrance Assessing Participant eligibility for testing Handling the queuing process Maintaining infection prevention standards during queuing Registering the Participant and adapting for disabled Participants/Participants without personal technology
Module 6: Train the trainer | This module includes the video introduction – to cover PPE, hand cleaning, the visual processing and analysis using LFDs and a talk-through the soft skills of delivery from a trainer. The trainer’s notes for delivery of a training session (these are very comprehensive and supportive) PowerPoint slides to support the session Handout to test the Sample Processor trainees’ understanding of LFD results A Sample Processors’ support document How to adjust a PPE ear-loop face mask to fit your face document A sign-off form for the Sample Processors they have trained Soft-skills trainers guidance
The table to the right provides a breakdown of the modules available on the online learning platform. Each of the modules provides information and guidance in a differing section of the testing journey, On the following slide, we have indicated which staff members will require completion of these specific modules.

## Slide 98: ACCESSING THE TRAINING PLATFORM
1
SET UP ACCOUNT:
Testing site staff will need to register using a unique token. The token and web link must be requested by emailing testertraining@dhsc.gov.uk. Once an account is set up, testing site staff will be able to access the online training at anytime.
Please find a token and the web link below:
Platform link: https://go.tessello.co.uk/TestDeviceTraining/
Token code: 3wkcVi4UTX

## Slide 99: TRAINING MODULES
2
ACCESS TRAINING MODULES:
Each module is split into two sections:
Information and guidance – (written content and training videos)
Assessment - multiple choice questions that the trainee will be required to answer
Each module takes approximately 15-30 minutes to complete. The questions in the assessment will test the trainee on information they have directly learnt from the information and guidance they have been provided within the module.

## Slide 100: COMPLETING TRAINING
3
COMPLETING TRAINING:
A 100% pass mark is required for the assessments. If the trainee fails the assessment, they will be able to refresh the module and repeat the read through of the content and resultant assessment. The trainee has unlimited access to these modules and there are no restrictions upon the number of times they can be accessed.
4
ADDITIONAL RESOURCES:
Testing site staff will have access to additional PDF resources. These files can be downloaded to the trainees platform and saved locally to their device for use offline.
These resources provide detailed content on a number of aspects that are crucial to testing and safety on site. If the trainees have any queries surrounding learnings in their module, we advise that they refer to the online resources for further information.

## Slide 101: REQUIRED ONLINE TRAINING
 | Module 1 LFD Process | Module 2 LFD results recording | Module 3 PPE & Infection control | Module 4 Guiding Participant through swabbing | Module 5 Meet and Greet | Module 6 Train the trainer
Team Leader | P | P | P | P | P | P
Registration Assistant | × | P | P | × | P | ×
Test Assistant | P | × | P | P | × | ×
Processing Operative | P | P | P | P | × | ×
Results recorder | P | P | P | × | × | ×
Queue Co-ordinator | × | × | P | × | P | ×
Other Role | × | × | P | × | × | ×
Online training modules for each staff member

## Slide 102: 5 DIGITAL
VERSION 2.5

## Slide 103: OPTIONS AVAILABLE:
A
DHSC PROVIDED DIGITAL SOLUTIONS
Test registration: Lite registration
Test Participant self-registers barcode for each test using their personal device (website)
Result capture: Log Results Website
Testing Operatives entering results using website on any device
Account setup: Organisation Admin Portal
A portal for Organisation Managers to set up testing sites and invite Team Leaders to manage them
Result delivery: Test Participant only
Test Participant receives SMS and email with result. Reported to National T&T, GP and Public Health of England (PHE)
Site finder: Local Authorities only
An online map providing information about the location, opening times and busyness of Asymptomatic Testing Sites to the public
B
ORGANISATIONS USE OWN DIGITAL SOLUTIONS
Organisations can choose to use their own digital solution to support their testing operation however this will have trade-offs and additional requirements on the organisation to fulfil.

## Slide 104: OVERVIEW
There are several different digital solutions offered by the DHSC that work together to enable the recording, uploading and notification of results.
They are used at different stages of the testing process.
5.1 BEFORE YOU START TESTING:
Organisation admin portal - A portal for Organisation Managers to create new testing sites (Site IDs) and invite Team Leaders
Team leader admin portal - A portal for Team Leaders at a testing site to securely manage access for testing operatives to log results
5.2 DURING TESTING:
Log results website - A website for Testing Operatives at a testing site to scan the barcode on a completed LFT test and submit its result to the relevant services.
Lite registration - Used to register a lateral flow test kit at a testing site. This creates a link between the sample ID/barcode and the person's details.
5.3 NOTIFICATION OF RESULTS:
Test and trace - The Test & Trace systems will link the test Participant’s registration record with their test result, by using the data from the “Lite Registration” and “Log Results” services.

## Slide 105: 5.1 BEFORE YOU START TESTING
Contents:
Overview
Onboarding
Organisation admin portal (For Organisation Managers)
Team Leader admin portal (For Team Leaders)
Internet connectivity on site

## Slide 106: OVERVIEW
Once digitally onboarded, organisations can set up new sites using the DHSC provided digital solutions.
There are two parts to this:
Use the ‘Organisation Admin Portal’ to setup your testing sites and Team Leaders
Use the ‘Team Leader Admin Portal’ to approve Testing Operatives, who will be recording test results at each site

## Slide 107: ADMINISTRATION SYSTEMS
 | LOG RESULTS – ORGANISATION ADMIN PORTAL For Organisation Managers A portal for Organisation Managers to Create new testing sites (Site IDs) and invite Team Leaders. | LOG RESULTS – TEAM LEADER ADMIN PORTAL For Team Leaders A portal for Team Leaders at a testing site to securely manage access for testing operatives to log results.
WHAT DOES IT DO? | Allows setup of a new site in the digital systems – allows selecting that site when registering and logging results Allows organisations to invite Team Leaders to administer a site | Enter a testing site ID Approve or revoke a ”Testing Operative" to record results at their site
WHEN DO YOU USE IT? | When setting up a new testing site When onboarding new Team Leaders When managing existing Team Leaders | When a new Testing Operative joins the team
HOW DO YOU START USING IT? | Receive an email invitation to the service from DHSC Click a link to activate account (by resetting password) | Receive an email invitation to the service from their Organisation Manager Click a link to activate account (by resetting password)
HOW DO I ACCESS IT? | Visit http://log-coronavirus-test-site-results.service.gov.uk/ and select "I'm an Organisation Manager" | Visit http://log-coronavirus-test-site-results.service.gov.uk/ and select "I'm a Team Leader"
OVERVIEW:

## Slide 108: TEAM LEADER DEVICES
REQUIRED DEVICE SECURITY CRITERIA:
The device is up to date (released within the last 2-3 years with the latest update applied)
The browser used on the device is up to date (the latest available update is applied)
The device is not compromised (e.g. “jailbroken” for iOS and “rooted” for Android).
The device is locked with a password, pin or biometric (eg. finger print or facial recognition).
The device is configured to time-out and lock after a period of inactivity.
The device is registered with a service that allows it to be found and/or wiped if lost or stolen
LOST OR STOLEN DEVICES:
Consideration for actions to be taken when a device is lost or stolen should be made as part of the site risk assessment.
Lost or stolen devices should be reported to the Site Manager as soon as possible and the account associated with the device deactivated.
DEVICE SECURITY
As Team Leaders can enable scanning operative accounts, the devices used by administrators pose an additional risk. Therefore, the following criteria must apply to the devices of Team Leaders.
NOTE: As Site Managers are automatically added as Team Leaders, this also applies to their devices.

## Slide 109: LOG RESULTS: ACCOUNT SETUP
ACCOUNT PROVISIONING AND SITE SETUP
For organisations to set-up an account to manage access to the Results logging digital tools, send your request to lftadminoperations@timeforstorm.com
NOTE: Org account creation requests may take up to 48hrs to process and can only be processed on weekdays.
In your email, provide the following information:
Organisation Name: Your organisation’s name
Organisation Contact: Your full name
Organisation Contact Email: Email address
Organisation Contact Phone Number (“+44” plus 10 digits, e.g. +447845634723)
FUNCTIONALITY
Following account setup, team leads will be able to:
Allow Team Leaders to add/remove account access for testing operatives to log the testing sites they manage
Allow testing operatives to scan and submit Lateral Flow test results
ONBOARDING
NOTE: The log results app will only work with accounts set up via this process. The site leader and team leader accounts previously created will not work with the Results logging virtual tools.

## Slide 110: INTERNET CONNECTIVITY ON SITE
INTERNET ACCESS:
Mobile data should be used by default
Wi-Fi may be used if mobile data is not available
WI-FI CONSIDERATIONS:
If you are setting up a new Wi-Fi network, we suggest using a SSID that not does not identify this is being for Testing activities.
Additional guidance can be found at https://www.gov.uk/guidance/sharing-workplace-wireless-networks

## Slide 111: ORGANISATION ADMIN PORTAL (FOR ORGANISATION MANAGERS)
BEFORE YOU START TESTING:

## Slide 112: INVITATION
RECEIVE INVITE FROM THE DHSC:
Receive an email invite from DHSC to create an account for your organisation, along with a text message confirming the temporary password for the account.
Selecting the link in the email will open the Testing Site Results service.
1
ORGANISATION ADMIN PORTAL:

## Slide 113: FIRST TIME ACCOUNT SET-UP
LOGIN AND UPDATE PASSWORD:
Select “I’m an Organisation Manager” and log in with the temporary password received in the text message. First time users will need to change their password to complete setup of their account. A code will then be sent to your mobile number for authentication.
Passwords must contain:
A lower case letter
An upper case letter
A special character
A number
At least 8 characters
2
ORGANISATION ADMIN PORTAL:

## Slide 114: ORGANISATION OPTIONS
MANAGE ORGANISATION OPTIONS:
Organisation Managers have the option to create new testing sites or to add and manage Team Leaders.
3
ORGANISATION ADMIN PORTAL:

## Slide 115: ADDING TESTING SITES
ADD TESTING SITES:
Organisation Managers can add new testing sites to their organisation. This will generate a Site ID and allows test Participants to select the testing site during registration. Site IDs may take a few hours to become active in Lite Registration.
ORGANISATION ADMIN PORTAL:
4
IMPORTANT GUIDANCE ON SITE IDs
A unique site ID must be created for each physical location where a test is conducted.
  It is not permitted to use a single site ID for a mobile testing operation
  This ensures that the appropriate action can be taken to trace contacts and contain outbreaks
Multiple Site IDs can be created for the same physical site if it is shared between multiple testing operations e.g. two schools testing in the same school hall
  The appropriate operational guidance needs to be provided to ensure results are logged and Participants register with the correct site ID

## Slide 116: ADDING TEAM LEADERS
ADD TEAM LEADERS:
Organisation Managers can add new Team Leaders to their organisation. Team Leaders can manage testing operatives at testing sites within the organisation.
Additionally, Organisation Managers are automatically allocated as a Team Leader.
ORGANISATION ADMIN PORTAL:
5

## Slide 117: MANAGING TEAM LEADERS
UPDATE TEAM LEADERS:
Organisation Managers can update information about existing Team Leaders within their organisation by selecting the ‘Manage’ link next to the Team Leader.
Saving a Team Leader as inactive (by deselecting the ‘Active’ radio button) will restrict them from logging into the Team Leader Admin Portal.
6
ORGANISATION ADMIN PORTAL:

## Slide 118: TEAM LEADER ADMIN PORTAL (FOR TEAM LEADERS)
BEFORE YOU START TESTING:

## Slide 119: INVITATION
RECEIVE INVITE FROM ORGANISATION MANAGER:
A Team Leader will receive an email invitation when they are added by the Organisation Manager. The email will contain instructions to access the Log Results Team Leader Admin Portal, along with a text message confirming the temporary password for the account.
Selecting the link in the email will open the Testing Site Results service.
1
TEAM LEADER ADMIN PORTAL:

## Slide 120: ACCOUNT SET-UP
LOGIN AND UPDATE PASSWORD:
Select “I’m a Team Leader” and login with the temporary password received in the text message. First time users will need to change their password to complete setup of their account. A code will then be sent to your mobile number for authentication.
Passwords must contain:
A lower case letter
An upper case letter
A special character
A number
At least 8 characters
TEAM LEADER ADMIN PORTAL:
2

## Slide 121: TESTING SITE SELECTION
TESTING SITE SELECTION:
Enter the site ID of one of the organisation’s testing sites and select ‘Continue’ to manage it.
3
TEAM LEADER ADMIN PORTAL:

## Slide 122: TESTING SITE MANAGEMENT
4
MANAGE TESTING SITE OPTIONS
Team Leaders have the option to manage new Testing Operative access requests for the site, as well as to view and manage the Testing Operatives who currently have access to the testing site.
5
TEAM LEADER ADMIN PORTAL:
TESTING OPERATIVE SITE ACCESS REQUESTS
Team Leaders can view, approve and deny new site access requests from Testing Operatives. If approved, the user's access will be displayed in the Current Site Staff list.

## Slide 123: MANAGING CURRENT SITE STAFF
CURRENT SITE TESTING OPERATIVES
Team Leaders can view, remove and re-approve site access for current Testing Operatives, with the current status of each operative shown via inline 'Approved' or 'Inactive' status.
6
TEAM LEADER ADMIN PORTAL:

## Slide 124: 5.2 DURING TESTING
Contents:
Overview
Uploading Test Results (For Testing Operatives)
Test Kit Registration (For Participants)

## Slide 125: OVERVIEW
DURING TESTING:
 | UPLOADING TEST RESULTS | TEST KIT REGISTRATION
 | LOG RESULTS WEBSITE For Testing Operatives A website for Testing Operatives at a testing site to scan the barcode on a completed LFT test and submit its result to the relevant services. | LITE REGISTRATION For testing participants Used to register a lateral flow test kit at a testing site. This creates a link between the sample ID/barcode and the person's details.
What does it do? | Request approval to log results at a testing site Record test results, once approved | Register their test kit Provide personal and contact details to be notified of their test result
When do you use it? | During shift at testing site | Each time they are tested at a testing site (can be fast tracked with an NHS account)
How do you use it? | Visit the URL Sign up by creating a username and password Sign in and enter a testing site ID Request and await access to the start logging results | Visit URL given at testing site (on registration card) Assistance can be provided for individuals who need help
There are two digital solutions that support the testing process when Organisations open and run their testing sites:
Log Results Website: For Testing Operatives to upload a Participant’s test results to the national T&T programme
Lite Registration: For Participants getting tested to register their unique sample ID/barcode

## Slide 126: UPLOADING TEST RESULTS (FOR TEST OPERATIVES)
DURING TESTING:

## Slide 127: LOG RESULTS WEBSITE OVERVIEW
LOG RESULTS WEBSITE:
The "Log Results" website is accessible via laptop, tablet or smartphone; enabling Testing Operatives to input and communicate results to participants and mandatory organisations
DEVICE OPERATING REQUIREMENTS:
Staff can use any smartphone, tablet or laptop that is securely connected to the internet (a camera is preferrable to enable quicker results submission, but it is not mandatory)
The device may be provisioned by the organisation (e.g. a council) or by the testing operative, e.g. using a personal device by a staff member
As each testing operative will need a device whilst working their shift to access the Log Results Website, the number of devices required for the site is dependent on the size of the workforce
The DHSC can provide managed devices with a pre-installed “Log Results” app if Organisations are not able to provide their own devices, Organisations should speak to their DHSC representative to request this, additional guidance about the ”Log Results” app is available in the Appendix
UPLOADING TEST RESULTS:
MINIMUM BROWSER REQUIREMENTS |  | 
DESKTOP | MOBILE (ANDROID) | MOBILE (IOS)
Chrome 57+ | Chrome 59+ | -
Safari 11+ | - | Safari 11+
Firefox 52+ | Firefox 55+ | -
Opera 44+ | - | -
 | - | -
The log results website will only work with Testing Operative’s accounts. The site leader and team leader accounts will not work with the Results logging virtual tools.

## Slide 128: TESTING OPERATIVE DEVICES
DEVICE SECURITY CRITERIA:
The device is up to date (released within the last 2-3 years with the latest update applied)
The browser used on the device is up to date (the latest available update is applied)
The device is not compromised (e.g. “jailbroken” for iOS and “rooted” for Android).
The device is locked with a password, pin or biometric (eg. finger print or facial recognition).
The device is configured to time-out and lock after a period of inactivity.
The device is registered with a service that allows it to be found and/or wiped if lost or stolen
LOST OR STOLEN DEVICES:
Consideration for actions to be taken when a device is lost or stolen should be made as part of the site risk assessment.
Lost or stolen devices should be reported to the Site Manager as soon as possible and the account associated with the device deactivated.
DEVICE SECURITY
The scanning process is designed not to process any personal data on the devices used by scanning operatives. However, the following criteria should apply to the devices of scanning operatives.

## Slide 129: PREPARING THE DEVICE
LOG RESULTS WEBSITE:
The Testing Site Operative must choose 'I'm a testing site operative' on the starting page (http://log-coronavirus-test-site-results.service.gov.uk/ ) and proceed to 'Sign in' using their username and password. If it is their first time accessing the website, they will need to select “Sign up” to create their username and password.
1
TESTING SITE LOCATION:
The Testing Site Operative then selects the testing site location they will be logging results at on the selected day. This is a 4-character Site ID and will be provided by the Team Leader. Confirming this will send a request through to the Team Leader to approve.
2
LOGGING TEST RESULTS PROCESS:

## Slide 130: WAIT FOR APPROVAL
GETTING APPROVAL
The 'Awaiting approval' page will be updated automatically when the user has been given access by their Team Leader. It will then allow them to start logging test results.
3
LOGGING TEST RESULTS PROCESS:

## Slide 131: SCANNING RESULTS
SCAN BARCODE:
The Testing Site Operative positions the device scanner so that the barcode sits within the box. When the barcode is scanned successfully, they will be directed to the next page to log result.
There is an option to enter the barcode manually if the scanner is unable to capture the barcode. The user will have to enter the barcode twice to ensure data accuracy.
4
LOGGING TEST RESULTS PROCESS:

## Slide 132: SUBMITTING RESULTS
ENTER RESULTS:
The Testing Site Operative selects the result of the test, and selects continue.
5
6
REVIEW AND SUBMIT RESULTS:
A summary of the test result is shown to the Testing Site Operator before they can submit the result. The Testing Site Operative can change both the barcode and the Test result using the 'change' buttons. Once they are confident with the result they can 'Save and continue' and will be shown a successful 'Test result logged' page if the result was successfully submitted.
LOGGING TEST RESULTS PROCESS:

## Slide 133: SIGNING OUT
SIGN OUT:
When the Testing Site Operative finishes their shift or hands the device over to another Testing Site Operative they must Sign Out. This can be seen at the top left of each screen
6
LOGGING TEST RESULTS PROCESS:

## Slide 134: TEST KIT REGISTRATION (FOR PARTICIPANTS)
DURING TESTING:

## Slide 135: LITE REGISTRATION OVERVIEW
Lite Registration is the digital solution for matching Test Participants to their LFD result
Participants are required to access the dedicated URL and enter their personal details and test kit barcode each time they are tested https://gov.uk/enter-lateral-flow-test
Participants can create accounts that save their details, so that they do not need to enter them the next time they get tested
Participant registration may take between 5-15 mins per participant depending on the questions that they have to answer for their circumstance, their digital literacy, and whether they have a “NHS Login” account or not.
TEST KIT REGISTRATION:

## Slide 136: REGISTRATION DEVICES
OVERVIEW:
Participants are encouraged to use their own mobile devices for the registration process
Organisations themselves can choose to provide devices for registration
Registration can be completed on any device (Computer, tablet, phone) with an internet connection and browser
The device should be corporation managed and configured so Participants cannot use it for any other purpose
DEVICE SETTINGS
Any device used to support the registration process will have to be operated in ‘incognito’ mode (this is to protect the privacy of the participants, as it will prevent users going back to previous form entries or seeing form auto-fills with personal information)
Devices should have antivirus software installed if possible
Where possible devices should be operated in “Kiosk mode” to prevent them being used for any other purpose
Registration devices are optional devices that Organisations can provide for Participants to register their test kit barcodes during the testing process.
TEST KIT REGISTRATION:

## Slide 137: ONLINE PORTAL
1
2
START REGISTRATION:
Participants need to register their unique barcode at http://gov.uk/enter-lateral-flow-test. This process will link them to their test sample and collect their contact details. Participants should the guidance and tap “Start now”.
REGISTRATION TYPE:
Participants can register a test kit for themselves or on behalf of another Participant.
LITE REGISTRATION PROCESS:

## Slide 138: ACCOUNT REGISTRATION
ACCOUNT REGISTRATION:
Participants can create and account or log into their account by tapping “NHS Continue with NHS login”. If the Participant does not want to create an account, they can tap “Continue without NHS login”.
3
Participants who do not want to create an account can skip to step 6.
LITE REGISTRATION PROCESS:

## Slide 139: NHS LOGIN PORTAL
4
NHS LOG IN:
If a Participant continues to “NHS Log in”, they will be asked to enter their email address. The system will check if the Participant has an account. If they have an account they will be asked for their password.
If they do not have an account, they will need to provide their mobile number to complete account registration.
LITE REGISTRATION PROCESS:

## Slide 140: ACCOUNT HOMEPAGE
ACCOUNT HOMEPAGE:
After the Participant logs into their account, or completes their NHS account registration, they will be taken to their account homepage. From here they Participants can register their latest test kit.
5
LITE REGISTRATION PROCESS:

## Slide 141: TESTING SITE SELECTION
TEST TYPE:
Participants need to select “At a testing site”.
6
TESTING SITE ID:
Signage with the site ID should be put up around the site to support the Participants as they register.
7
LITE REGISTRATION PROCESS:

## Slide 142: BARCODE AND TEST DETAILS
UNIQUE BARCODE:
Participants then need to scan or manually enter their unique test barcode, this will link the participant’s test sample to their personal details.
8
LITE REGISTRATION PROCESS:

## Slide 143: BARCODE AND TEST DETAILS
DAILY CONTACT OR REGULAR TESTING:
Participants then need to select whether they are testing as part of a daily contact or regular testing regime, more details on this can be found in the “Clinical, protocol & policy” section of the Guidebook
9
DATE AND TIME OF TEST:
The Participant will then be asked to enter the date and time that they are taking the swab sample.
Participants with accounts, who have previously gone through this process and registered a test kit can skip to step 12.
10
LITE REGISTRATION PROCESS:

## Slide 144: ADDITONAL DETAILS
ADDITONAL PERSONAL DETAILS:
Participants will need to provide the following details:
Name
Gender
Date of birth
Ethnic group
Details of recent travel to work or place of education
Depending on what a Participant answers to certain questions, they may be required to answer additional questions.
COVID SYMPTOMS:
Participants need to confirm if they have Covid symptoms.
Participants with accounts, who have previously gone through this process and registered a test kit can skip to step 14.
12
11
CONTACT DETAILS:
Participants will need to provide the following details:
Contact email
Contact mobile phone number
Home address
13
LITE REGISTRATION PROCESS:

## Slide 145: TEST KIT REGISTRATION COMPLETE
14
REGISTRATION COMPLETE:
The Participant has now completed registration for their test kit.
LITE REGISTRATION PROCESS:

## Slide 146: 5.3 NOTIFICATION OF TEST RESULTS
Contents:
Overview
Positive Test Result
Negative Test Result
Void or Invalid Test Result

## Slide 147: OVERVIEW
The Test & Trace systems will link the test Participant’s registration record with their test result, by using the data from the “Lite Registration” and “Log Results” services.
RECEIVING THE RESULT:
Result will be sent to the Participant via SMS and/or e-mail
Results will be communicated within a day of the test
NOTIFICATION OF TEST RESULTS:

## Slide 148: POSITIVE TEST RESULT
NOTIFICATION OF TEST RESULTS:

## Slide 149: NEGATIVE TEST RESULT
NOTIFICATION OF TEST RESULTS:

## Slide 150: VOID OR INVALID TEST RESULT
NOTIFICATION OF TEST RESULTS:

## Slide 151: 5.4 DIGTIAL ACCESSIBILITY
Contents:
Overview
Engagement Channels
Assistance Organisations Can Offer
Services Available
Protocol For Providing Assistance

## Slide 152: OVERVIEW
A SUCCESSFUL DEPLOYMENT CONSIDERS THOSE WITH:
Low digital literacy
Low English literacy
No access to a phone or email
A diversity of physical and mental conditions
Low confidence and propensity to isolate
THE LATEST KEY STATISTICS SHOW THAT:
10% of households have no internet access
7.5% of people have never used the internet
4% of UK adults do not have a phone
22% of UK adults do not have essential digital skills for day-to-day life
A significant number of people (approx. 15 – 20%) have to been excluded from testing services due to being digitally excluded.
Non-digital access to the service is essential to ensure these groups have equal access to testing. A number of participants are more susceptible to being excluded of the digital testing services.
DIGITAL ACCESSIBILITY:

## Slide 153: ENGAGEMENT CHANNELS
GENERAL GUIDELINES:
Clearly communicate the rationale and the importance of regular testing
Clearly communicate how the testing process works and what is involved
Assure participants on data and physical security measures in place
EXAMPLE MEDIA:
Analogue news media
Printed media
Trusted communities
GPs/ 119 advice
Local amenities
Research shows that, to date, the most effective way of communicating with digitally excluded participants is to use more traditional media in more languages.
DIGITAL ACCESSIBILITY:

## Slide 154: ASSISTANCE ORGANISATIONS CAN OFFER
FACE TO FACE ASSISTANCE:
A private, secure area, should be in place to allow for face to face assistance
Staff on site should assist participants by entering data into the digital registration journey on their behalf (with consent)
Ideally staff on site will cover a diverse set of languages
LENDING DEVICES:
Spare electronic devices (smartphone, tablet or PC with internet connectivity) should be on hand to lend to participants to complete registration
Offering sanitiser and regularly wiping the device will help minimise the spread
Personal data must not be saved on the device
TRANSLATED PRINT MEDIA:
Media on site should be translated into various languages, some of these are available centrally (see Comms & Engagement section).
Laminating and regularly wiping the print can help minimise the spread.
A range of services should be provided to (but not limited to) digitally-excluded participants across their testing journey.
DIGITAL ACCESSIBILITY:

## Slide 155: PROTOCOL FOR PROVIDING ASSISTANCE
Participant should be offered support and, if accepted, should be escorted to an area where they can be assisted privately
Here either provide a org-owned device to the participant and let them complete the registration on the device – being present in case of any questions. Or you can enter the information on their behalf. In this case you must always ask for consent before filling out the registration form on behalf of someone.
You should always encourage use of mobile number if possible, telling them is the best way to get results quickly. They can also use the mobile number of a Trusted Person who will receive their result for them.
Any issues, they can call 119, free to call from any phone
The protocol applies when a participant arrives with:
No digital device
No email or mobile number or is unwilling to give this information
DIGITAL ACCESSIBILITY:

## Slide 156: 5.5 TECHNICAL SUPPORT & TROUBLE-SHOOTING
Contents:
Overview
Digital Contingency Process
Troubleshooting Guide
Repeat LFT Results

## Slide 157: OVERVIEW
OVERVIEW:
Testing Operatives are encouraged to firstly seek local assistance with any issues relating use of devices and connectivity, logging in to the web service and the recording of results (e.g., the organisation's help desk)
Before reaching out for support, please ensure that your device is operating as expected in the first instance, and that it has a good data and/or wi-fi connection
The following section provides troubleshooting advice for a range of issues. Please refer to this FAQ before calling 1st Line Support
If you are unable to resolve the issue locally please request that the site Team Leader call 1st line support on 0203 281 6468 Operating hours are 07:00 – 20:00
You will need to provide the following summary information:
  Reporter Name: your name Reporter Organisation: your organisation’s name Reporter Tel: your mobile or landline number Reporter Site ID: the 4-digit alphanumeric reference Incident Description: an explanation of the issue with detailed guidance how to reproduce the issue
TECHNICAL SUPPORT & TROUBLESHOOTING:

## Slide 158: DIGITAL CONTINGENCY PROCESS
WHAT TO DO WHEN:
You are unable to use all or parts of the digital solution because:
The system is offline temporarily
You are not able to get access
OVERVIEW:
In the event of the digital solution being unavailable, there are three components that can be operated in an offline contingency process;
Participants are unable to register their barcode and personal details
Test operatives are unable to submit results
Results cannot be delivered to Participants due to either 1, 2 or an issue with the results delivery service
Temporary outage (e.g. Short term downtime or temporary no access)
Majority of operational processes remain the same with registration and results uploaded retrospectively once access is regained to the digital systems.
Record results manually offline
Operational process changes are required to deliver results directly to Participant in-person or record registration details offline to deliver results manually
Longer term outage (e.g. multiple days of no access)
All positive results must be reported within 24 hours
For outages longer than 24 hours, positive results must also be reported directly to Public Health England via the Laboratory Reporting process
Note: When using the contingency process, test results will be recorded at the time of retrospective entry rather than the actual date and time of the test. This impacts the reporting of national test results and therefore this should not be used as a “Business as Usual” process.
TECHNICAL SUPPORT & TROUBLESHOOTING:

## Slide 159: DIGITAL CONTINGENCY PROCESS
PARTICIPANT REGISTRATION | TEST RESULT CAPTURE | RESULT NOTIFICATION
When to move to this contingency process The Light Registration website is down or can’t be accessed by the Participant The Participant cannot access the website at the point of care (e.g. there is no internet) | When to move to contingency process The Log results website is down Lack of devices or equipment failure You have been unable to setup Org manager, Team leader or Test operative accounts in time | When to move to contingency process When the Participant Registration contingency process is in place When the Test result capture contingency process is in place
Operational process Give the Participant a registration card with their barcode on it to take away Instruct the Participant to follow the instructions on the card and attempt to register as frequently as possible until successful | Operational process: Continue to mark the test result with a marker on the LFD when reading the result Transcribe the barcodes and results into the Contingency process spreadsheet and store offline temporarily | Operational process option 1 - hold Participants for results As digital result delivery will be delayed, a process must be put in place to hold Participants after providing the test sample Keep the Participant and the LFD where the sample was taken until a result can be read Provide the test result verbally and visually at the point of test to the Participant with the current guidance on next steps (see section 3) Operational process option 2 – manual result delivery The testing sites can manually record the personal details of the Participant and their test barcode offline (e.g. spreadsheet containing name, barcode, result and contact details at a minimum) Once a result is known, Test Operatives can contact the Participant and inform them of their result manually
Retrospective recovery process Participants can register their test retrospectively, even after the result is submitted by the testing site The system will hold unmatched test results for up to 7 days while waiting for the Participant to register | Retrospective recovery process Once you have gained access to the Log results websites, enter the test results from the Contingency process spreadsheet. Positive results must be retrospectively uploaded within 24 hours. For outages longer than 24 hours, positive results must also be reported directly to Public Health England via the Laboratory Reporting process | Retrospective recovery process Once a Participant has been retrospectively registered and a result entered, the result will still be delivered digitally The Participant must be informed that a digital confirmation will follow, after they have been communicated their manual result
TECHNICAL SUPPORT & TROUBLESHOOTING:

## Slide 160: RISKS USING THE CONTINGENCY PROCESS
RISK | MITIGATION
Data privacy If using option 2 for result delivery, the testing site must consider how this handling of personal data impacts their current privacy statement. | For a testing site to store the personal details of a Participant offline (outside of NHS systems), they will need to consider a revised Privacy Statement and put in place the appropriate process in place to handle this data.
Human error – Data entry into spreadsheet When entering data such as barcodes and results it can be easy to make errors. | Testing sites should put in place a process to double check data entered into the contingency spreadsheet with a second Test Operative to minimise the risk of mismatched data. Testing sites should stop using the contingency process ass soon as the digital solution is available to use.
Human error - Result delivery from spreadsheet If results are being delivered from a spreadsheet, there is a risk that similar data or barcodes may be mismatched or mixed up, potentially causing the wrong result to be communicated. | Use option 1 for result delivery if it is operationally feasible. This allows the result to be communicated at point of care, reducing the risk of human transcription errors. If option 1 is not feasible, processes must be established to validate that the right result is being communicated to an individual.
Delayed result delivery Data entered retrospectively will appear as being done at time of entry rather than when the actual test was taken. This may have an impact on Management Information and national reporting if the contingency process is used for sustained period. | Testing sites must only use the contingency process as a last resort and must use the digital solution as soon as it is available.
TECHNICAL SUPPORT & TROUBLESHOOTING:

## Slide 161: TROUBLESHOOTING GUIDE 1
ISSUE | GUIDANCE | NEXT STEPS
I cannot get my device to switch on / I am having an issue with my device | Seek local support from Testing Site Team Leader or Site operator | 
I cannot find the internet browser on my device |  | 
I cannot connect to the internet |  | 
The website will not load | Is your device connected to the internet? Is the internet / site working for other colleagues around you? Can you see any error message displayed on your device? | Seek local support from Testing Site Team Leader or Site operator. If they are unable to resolve locally then please contact 1st line support for assistance on 0203 2816468
I cannot login at login screen | Have you entered your login details correctly? These are case sensitive. If you have forgotten your login details please refer to subsequent sections of this guide | Seek local support from Testing Site Team Leader or Site operator. If they are unable to resolve locally then please contact 1st line support for assistance on 0203 2816468
I have logged in but the website says “Awaiting approval” | After you have selected your Testing Site location, a Team Leader must approve you before you can start recording test results. | Check that a Team Leader at your location has done this for you
I am logged in as a Team Leader but cannot see a list of staff under the “View Staff” option | It may be that no staff have logged in to work at your Testing Site yet. Alternatively, there may be staff members waiting for a Team Leader to approve their access to your Testing Site. | Check under the “Manage new requests” page to see if you have any staff to approve
TECHNICAL SUPPORT & TROUBLESHOOTING:

## Slide 162: TROUBLESHOOTING GUIDE 2
ISSUE | GUIDANCE | NEXT STEPS
I am a Testing Operative - I do not remember my user name or password | Testing Operatives cannot reset passwords currently. If you are unable to log in to your account you will need to re-complete the “Sign up” process again to create a new account. This will also mean requesting access to your testing site again | Your Team Leader should be able to view your user name within the Team Leader Webservice “View Staff” page
I am a Team Leader – I do not remember my user name or password | Follow the password reset instructions visible on the login page | If the reset process does not resolve the issue speak with your Team Leader for further assistance
I don’t know the Testing Site ID | The Testing Site ID should be known by the Team Leader(s) and/or organisation responsible for the Testing Site | Speak with Team Leader and/or your organisation
I don’t recognise the Site name when I enter the Testing Site ID | Ensure you have entered the Site ID correctly. The Testing Site ID should be known by the Team Leader(s) and/or organisation responsible for the Testing Site | Speak with Team Leader and/or your organisation
I have logged in but am unable to use the webservice to record test results | Have your site access request been approved by your Team Leader yet? If you see the word “pending” by your chosen site when logged in you will not be able to log test results | Speak with Team Leader and/or your organisation
I cannot scan a barcode successfully | Please ensure the camera on your mobile device is working, e.g. in other applications on your phone Please ensure the scanning area is sufficiently illuminated and the barcode is clearly readable As a workaround, you can input the barcode manually. You will have to input the barcode ID twice to ensure no spelling mistakes. | Speak with Team Leader and/or your organisation
TECHNICAL SUPPORT & TROUBLESHOOTING:

## Slide 163: TROUBLESHOOTING GUIDE 3
ISSUE | GUIDANCE | NEXT STEPS
I am logged in as a Team Leader but cannot see a list of access requests to approve/deny | Ensure that the testing operatives of your testing site have successfully logged onto the service, and requested approval to be part of your testing site | If the issue prevails, speak to your organisation and ensure you have been onboarded
The barcode is not being accepted when I type it in manually | You will have to input the same barcode ID twice to ensure no spelling mistakes: once in the upper text input field, and again in the lower text input field. | 
I think I incorrectly logged the result for a person’s test | If you believe that you incorrectly submitted a result, make a note of the barcode, and see the process for “Repeat LFT results” on the next page. | See next page.
How do I sign out from the webservice? | The Sign out link is in the top left of each page | 
The camera on my device is not working / I do not have a camera I can use | You can upload results by entering the barcode manually via the keypad or keyboard of your device. | 
How do I know if I’m in the Team Leader webservice or a Testing Operative webservice? | The URL for the Team Leader webservice is: http://admin.log-coronavirus-test-site-results.service.gov.uk/ The URL for the Testing Operative webservice is: http://log-coronavirus-test-site-results.service.gov.uk/ | 
As a Team Leader, I need to revoke a testing operative's ability to access the service on my testing site | Within your dashboard, go to “View staff”. From here you can view every testing operative assigned to the testing site you manage. Team Leads can revoke access on an individual basis. | 
TECHNICAL SUPPORT & TROUBLESHOOTING:

## Slide 164: REPEAT LFT RESULTS
1
2
OPERATIVE ERROR RAISED:
The operative realises a mistake has been made and asks the Team Leader to re-scan the LFD with their device.
RE-SUBMIT RESULT:
Team Leader scans the LFD barcode with a device, selects the correct result, confirms details and submits result.
(If using the Log Results app, this step will need to be performed with a different managed device than the device used to scan the original result.)
CONFRIM RESUBMISSION:
When the Team Leader submits the result again, this will update the backend systems that an error was previously made.
3
119 CONTACTS Test Participant:
The Participant who had an incorrect result submitted may have already been notified of their incorrect result via SMS or email. 119 will contact the and inform them of next steps.
CORRECTION OF RESULT:
The backend systems will replace the previously incorrect result submission with the corrected result.
4
5
WHAT TO DO WHEN:
A Lateral Flow Test (LFT) barcode/sample ID has been submitted incorrectly to the result service via the Log Results app or website.
TECHNICAL SUPPORT & TROUBLESHOOTING:

## Slide 165: OPTION B: ORGANISATIONS USE OWN DIGITAL SOLUTIONS
OVERVIEW:
Organisations can choose to use their own digital solution to support their testing operation
In this case, the organisation is responsible for reporting test results to Public Health England directly
TRADEOFFS WHEN USING THE PHE SOLUTION:
Results will not be delivered to Test Participants
Positive tests will not trigger contact tracing
Test Participants details will not be matched to test results
There is no support provided from the DHSC, Test & Trace or any other NHS service if the organisation uses their own digital solution
SETUP:
To use the PHE reporting solution, organisations must contact poct.contact@phe.gov.uk and SGSS.helpdesk@phe.gov.uk to discuss the best way to provide data

## Slide 166: 6 Comms & ENGAGEMENT
VERSION 2.5
Pre-approved assets
Customer marketing, branding, and specialised assets
Encouraging participation
Community engagement

## Slide 167: PRE-APPROVED ASSETS
APPLICABILITY
Created and maintained centrally from insights gained across pilots
All organisations can use these pre-approved assets immediately
MINOR MODIFICATIONS
You can apply an organisation branding logo to the materials without seeking approval if required
Minor modification can be made to these assets but will require final approval by the central content team before they can be issued externally
All 3 categories of assets have been agreed centrally as suitable across a range of use cases without the need for tailoring. All of these assets can be shared externally immediately.
TYPES OF COMMS
Instructional and process comms: clinically-approved detailed guides for conducting testing
Organisational messaging comms: supporting organisations with Participant engagement addressing the ‘why’ and ‘how’
Public-facing campaigns: NHS branded, large scale marketing campaigns
EXAMPLES OF MATERIALS THAT CAN BE PRODUCED:
Adverts (marketing campaigns)
Web banners
Flyers
Animations
Storyboards
Copy (wording for comms)
Graphics
Posters
Videos (“How to swab” videos, training videos etc)
Signage (entrance signs, exit signs, booth number signs etc)

## Slide 168: CUSTOM MARKETING, BRANDING & SPECIALISED ASSETS
APPLICABILITY:
For use cases that are unique or significantly different to available comms
For applications that are high-profile, or of strategic and political importance and no assets exist already or where the messaging required is bespoke
FOR USE CASES:
Requests for custom assets be raised to the central comms working group by the DHSC mailbox p-and-psector@dhsc.gov.uk
Each request is prioritised based on capacity and has a creation lead time which will be confirmed when the request has been accepted
A design representative will work closely with your team and target organisation to create bespoke materials that fit your need
Where required, the central content team can create bespoke assets for an organisation. Requests are prioritised based on capacity

## Slide 169: ENCOURAGING PARTICIPATION
BARRIERS TO TESTING | WHO IS MOST LIKELY TO BE AFFECTED? (not exhaustive) | POTENTIAL MEASURES TO COMBAT THESE BARRIERS
Practical barriers to access – e.g. ability to: access a testing site; travel to a testing site; read or engage with testing materials; book a test via digital channels | Carers: ~10% of population People with disabilities: ~20% of population has a disability Vulnerable people e.g. homeless (0.5% of pop), victims of domestic abuse (~3%12), functionally illiterate (~16%13), non English speakers (0.3%14), etc. | Making testing sites easy to access –increase testing site opening hours; offer access to testing in additional locations e.g. test kit distribution from GP surgeries or pharmacies / hyper-local areas; in community locations (e.g. mosque) Design physical sites and testing materials with accessibility at the forefront – e.g. ramps for wheelchair users, instruction materials in multiple languages, non-digital routes to testing
Financial barriers – people are prevented from engaging with testing due to their own financial circumstances. Many may not wish to get tested out of fear of self-isolation and losing out on income | 20% population living in poverty - some BAME groups have higher rates of poverty in working adults e.g. Bangladeshi (50%), Pakistani (~45%), Black (38%), Chinese (34%) vs. White (20%); similar issue for disabled ~40% who don’t have enough savings to live for 1m without income | Offer financial rewards for participation (e.g. monetary payments, discounts or subsidised travel costs) Greater communication of support offers for people in self-isolation (e.g. £500 Test and Trace support payment or locally led support networks)
Lack of knowledge to engage with Test and Trace in the desired way – e.g. does not understand why testing is important or how to access services | Population wide issue, but likely to particularly affect people with low English or literacy skills | More targeted communications through community leaders about how people can access testing services and why this is important to combat Covid Promote testing amongst community sites

## Slide 170: ENCOURAGING PARTICIPATION
BARRIERS TO TESTING | WHO IS MOST LIKELY TO BE AFFECTED? (not exhaustive) | POTENTIAL MEASURES TO COMBAT THESE BARRIERS
Lack of trust in Test and Trace and / or the Government – e.g. does not believe that Test and Trace will work so why bother, unwillingness to share personal information with the Government | People who feel they have been treated badly by state previously e.g. BAME ~14% of pop. People who get their news from social media – more likely to be male (58% UK users) and young (80%+ 18-34) | More targeted communications of Test and Trace success stories in local communities Engagement with local networks and community leaders to promote the testing service – e.g. in sermons, churches, mosques
Apathy to Covid-19 – does not perceive a threat to self and / or does not care about threat to others | Young are less likely to be very worried about Covid Men are more likely to believe it is not a threat to them Those who think they have already had the virus Those who feel culturally alienated and separated from mainstream society | Targeted communications on impact of own behaviours on others – e.g. what is the impact of mask wearing? How can apathy negatively impact on loved ones? Greater promotion of testing through institutions – e.g. universities / workplaces / schools

## Slide 171: COMMUNITY ENGAGEMENT
BETTER COMMUNICATION OF AVAILABLE SERVICES:
To combat lack of awareness, the purpose and outcome of testing should be clearly communicated. For example, how someone can access a test? How does getting tested contribute to ‘a return to normality’?
There should be strong promoting and sign-posting to support services available within a local community, such as the £500 Test and Trace Support Payment for people in self-isolation https://www.gov.uk/test-and-trace-support-payment , or local support networks (e.g. buddies or food shopping help)
1
OFFICIAL SENSITIVE – DO NOT SHARE FURTHER WITHOUT PERMISSION – SUBJECT TO LEGAL, REGULATORY AND POLICY REVIEW
Whilst communications and engagement will not alone generate a significant increase in the take up of testing, there are practical steps to take to better communicate its purpose to the wider public.
FOCUS ON ‘CIVIC DUTY’:
There are benefits from generating a sense of ‘civic duty’ and personal and group solidarity in relation to mass testing.
The Liverpool mass testing pilot demonstrated that messaging around protecting loved ones, ‘saving Christmas’ and protecting the NHS were effective lines of messaging to incentivise uptake of testing.
Dependent on the targeted community, this line of messaging on enabling celebrations should be tailored to suit different cultural needs – e.g. Eid, Diwali, Chinese New Year
2

## Slide 172: COMMUNITY ENGAGEMENT
ACCESSIBLE MATERIALS:
As discussed on earlier slides, it is important for communications to be offered in multiple languages and in accessible formats (e.g. braille, British Sign Language) to ensure penetration within certain demographics.
If reading skills are limited, consider using audio files or videos.
COLLABORATION WITH LOCAL COMMUNITIES:
The co-production of health messaging with the target community is important to ensure appropriate and tailored messaging.
For example, case studies from the local community and relevance to cultural norms (e.g. weddings or different cultural celebrations).
Respected community figures (e.g. local health professionals, religious leaders, charitable organisations) should be utilised to provide guidance and advice on how to reach certain communities, and promote the testing service.
3
4

## Slide 173: APPENDIX: LEGAL, QUALITY & RISK MANAGEMENT

## Slide 174: DAILY CONTACT TESTING ORGANISATION OBLIGATIONS
ORGANSIATION OBLIGATIONS:
The organisation must identify the close contacts of the positive case
The organisation must get permission for participants who wish to be involved in daily contact testing and those that do not
The organisation should update Trace through the service hub for participants involved in daily contact testing
The organisation is responsible for managing the daily contact testing rota of their employees.
NOTE: USE OF DAILY CONTACT TESTING IS RESTRICTED TO ORGANISATIONS ACCEPTED UNDER THE DAILY CONTACT TESTING PROGRAM
Notes: E2e process in sub
Add training into 2

## Slide 175: PARTICIPANT DATA, PRIVACY & CONSENT
OVERVIEW:
Participants will be required to register their details online and give consent for NHS Track and Trace to process their data and contact them with their results.
Participants do not have to legally share their test results directly with Organisations, however they are obliged to inform their organisation if they test positive. If Organisations want Participants to share their results, they are responsible for getting their consent.
ORGANISATIONS WILL BE REQUIRED TO:
Communicate the purpose of testing and the testing journey
Direct Participants to the Data Privacy Notice which explains how NHS Test and Trace will use their data (https://www.gov.uk/government/publications/coronavirus-covid-19-testing-privacy-information)
175

## Slide 176: DEFINITIONS
QUALITY MANAGEMENT (IN THE CONTEXT OF TESTING INCLUDES):
Keeping the environment safe
Making sure staff are trained and competent
Performing testing audits and monitoring KPIs to ensure clinically accurate testing is delivered
Maintaining a positive experience and outcome for Participants
Communicate the purpose of testing and the testing journey
RISK AND ISSUE MANAGEMENT
The identification of risks and appropriate plans to avoid or reduce the risks. Effective management of quality and risks at a testing station is important to:
Mitigate risks
Manage adverse events safely, and openly investigate
Learn and improve
QUALITY ASSURANCE ASSESSMENT
Each testing site will perform an agreed number of dual PCR and LFD swabs on their participants to compare the accuracy of testing
Analysis will be performed at an aggregate level for the archetype as a whole, and not for individual sites.
The quality assurance swabs will be sent to the laboratory for analysis and matching against the LFD results for comparison
This quality assurance measure is completed in addition to any confirmatory PCR test that may be in place for the testing site, and may be repeated to ensure clinical assurance

## Slide 177: RESPONSIBILITIES
WHO IS RESPONSIBLE:
Everyone involved in testing has a responsibility to maintain quality and manage risk, however the Team Leader is ultimately responsible.
A designated team member will need to act as the Quality and Governance Lead, who can be the Team Leader, and have accountability for the clinical quality and risk management of the service.
KEY ACTIVITIES:
It is expected that good quality and risk management processes are put in place covering areas such as:
Managing the completion daily and weekly site setup checklist
On-going availability of training materials for site operators
Monitoring of key results and KPIs applicable to the testing site
Managing health & safety and security of site
Clear and communicated point of escalation for issues on site, and a route to escalating to local public health officials as appropriate
Ensure adherence to the Standard Operating Procedure
Respond to any data privacy concerns as directed
Clinical governance and quality assurance accountabilities should be defined before starting the testing

## Slide 178: SUGGESTED PRACTICES & TOOLS
QUALITY CONTROLS:
Operational checklist: A daily/weekly checklist for team leaders to use to ensure testing site materials and procedures are ready for safe testing
Workflow reviews: Assessment of relevant workflow on a periodic basis and following any incidents
Staff training: Observational assessment of staff carrying out the testing process and completion of training records, including updates to training
Monitor void tests: Investigating reasons where occurring, especially in cases of repeated occurrences or higher than usual numbers
Incident reporting: Defined incident reporting process and log – see appendix for incident log template and DHSC contact points
RISK ASSESMENT & REGISTER:
All sites should conduct a risk assessment completed prior to launch. The assessment will be specific to the circumstance of the testing operation and should identify the nature of the risk, severity and likelihood of it occurring and the actions to mitigate.
All sites should have a risk register that is maintained, updated and reviewed regularly (typically daily), ideally by the Team Lead. The register should build on the initial risk assessment.
Each site should develop a plan on how they will go about managing quality, risks and issues. The below are common practices and tools that can be used to deliver the plan.

## Slide 179: SAFETY AND INFECTION PREVENTION RISKS
CONSIDERATIONS:
Ensure the area and equipment cleaning is carried out thoroughly between each sample
A clinical waste bin is nearby and easy to reach
All cleaning equipment and a supply of fresh replacement PPE are present and ready for use
PPE is donned fully and correctly
Infection prevention and control procedures are in place and understood
Social distancing is maintained throughout the operation
Hand-washing and cleaning procedures are carried out
Adequate signage to ensure Participants comply with one-way flow and socially distanced queueing.

## Slide 180: TESTING PROCESS RISKS
CONSIDERATIONS:
The 30-minute reading is a strict deadline. Reading results after 30 minutes can give a false positive.
Do not let the extraction fluid bottle touch the extraction tube when adding the 6 drops (to prevent cross-contamination)
Do not touch the sample well at any point – this is a specific risk during the application of the barcode label on the back of the cartridge
Check the cartridge is in date
Ensure you complete 10 seconds’ worth of extraction of the sample
Ensure the 2 drops of extracted sample fluid are bubble-free before releasing them into the sample well
The recording of results is double-checked before submitting
The LFD is stored on a flat surface while processing and not moved
The LFD devices and reagents need to be stored between 15 and 30oC during use. Appropriate temperature monitoring and control will be necessary to ensure this

## Slide 181: TEAM AND RUNNING THE SITE RISKS
CONSIDERATIONS:
Self-swabbing and testing overall may be a new experience for many people and they may be anxious. Participants should not be hurried and swab at their own pace
Testing and operations teams understand and self-enforce rules related to eating and smoking while on breaks
The testing team are aware of how to raise risks or issues
No one associated with BAU activity should be permitted access to the testing site unless they are involved in the day-to-day running of testing site operations
Social distancing is maintained throughout the testing operations by both Participants and testing teams
Where space is limited, test queues are managed safely to avoid disruption – for example, a waiting room may be separate and adjacent to a testing room and must allow for appropriate social distancing
The testing area, sample collection stations and privacy booths should be easy to clean and sterilise

## Slide 182: APPENDIX: JOB DESCRIPTIONS

## Slide 183: JOB DESCRIPTIONS: TEAM LEADER
Opens and closes site each day, including making the daily Go/No Go on testing operations
Runs day-to-day operations including on-site workforce management, managing site health & safety and receiving and managing stock
Point of escalation for any issues on site, escalates to local public health officials as appropriate
Provides people support to Site and Test Operative roles
Ensures all resource have arrived for shift and escalates no shows
Cascades new information to all team members
Ensures adherence to SOP and clinical guidance is maintained throughout operations
Responsible for the quality and risk management of the testing and regularly checking that the site meets the standards required
Job Title
Team Leader
Job Overview
The Team Leader is responsible for the overall on-site operations of the testing site, including delivery of testing services, ensuring adherence to health and safety protocol and day-to-day workforce management.
Responsibilities & Duties
Preferred Experience
Desired Skills and Traits
Experience overseeing an operational workforce and day-to-day people management
Experience in managing compliance against regulatory guidelines preferred
Experience managing operations in a Participant facing environment
Candidates with management experience at events and or in leisure and hospitality settings would be highly suitable
Demonstrated ability to lead multi-faceted teams in a fast changing environment
Strong stakeholder management and communication skills
Problem solving skills with strong ability to make quick decisions
Ability to keep calm under pressure

## Slide 184: JOB DESCRIPTIONS: SITE OPERATIVE
Ensures social distancing is maintained in Participant queueing areas and identifies and asks symptomatic Participants to leave the site
Greets Participants at arrival, asking them to sanitise hands and ensures the Participant is eligible for testing
Directs Participant to available testing stations and then the following completion of swabbing
Provide verbal instruction on how to complete self-swabbing
Deals with Participant queries, and supports Participants with accessibility requirements as appropriate
Supports general site set up and maintenance, including supplies management and regular cleaning of testing stations throughout the day
Job Title
Site Operative
Job Overview
The Site Operative is a Participant-facing role responsible for supporting the Participant through the end-to-end testing experience and supporting wider site operations. Working across a number of positions, key activities include managing social distancing through orderly queuing, supporting Participants through registration, providing verbal guidance on the testing process and regular cleaning of the site.
Responsibilities & Duties
Preferred Experience
Desired Skills and Traits
Experience in a fast-paced, Participant-facing environment
Experience working with members of the public/patients, preferably including crowd control
Experience working at events and leisure & hospitality
Demonstrated strong interpersonal skills – facilitating the ability to give clear and concise instructions
Demonstrated ability to work flexibly – providing support across different roles where necessary
Strong attention to detail and communication skills
Fairly digitally savvy (for use of the on-site application)
Must be able to thrive in a fast-paced environment and physically stand for several hours

## Slide 185: JOB DESCRIPTIONS: TESTING OPERATIVE
Receives sample and prepares for analysis, including application of reagent
Times sample and indicate when ready for sample analysis
Reads the result on test device and marks result on device
Enters result onto a digital or manual solution
Ensure safe clinical measures, including practicing of social distancing and donning and doffing of PPE, of all times
Job Title
Testing Operative
Job Overview
The Testing Operative supports the preparation and analysis of test samples, and recording of results. The safety of the workforce and Participants is the foremost priority for all testing operations; full PPE and strict infection control measures will be employed in order to ensure a safe working environment at all times
Responsibilities & Duties
Preferred Experience
Desired Skills and Traits
Experience in clinical settings preferred but not essential
Experience in understand and following Standard Operating Procedures
Experience with data recording/entry - comfortable using digital technology to record results
Strong interpersonal skills and ability to work under pressure in a fast paced environment
High attention to detail and strong time keeping skills
Ability to follow the strict guidelines and procedures required
Must be able to thrive in a fast-paced environment, including physically standing for protracted periods

## Slide 186: APPENDIX: WORKFORCE RESOURCE REQUIREMENTS

## Slide 187
 |  | Number of Testing Stations (Testing Site Size) |  |  |  |  |  |  |  |  |  |  |  |  | 
Role | Position | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14
Team Leader |  | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
Site Operations Role | Queue Coordinator** | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 1
 | Registration Assistant | 0 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 2 | 2
 | Test Assistant*** | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 2 | 2 | 2 | 2 | 3
Testing Operations Role | Processing Operative | 1 | 1 | 2 | 3 | 4 | 4 | 5 | 6 | 6 | 7 | 8 | 8 | 9 | 10
 | Results Recorder | 0 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 2 | 2 | 2 | 2
Break & Absence Cover (8 hrs operations) |  | 0 | 0 | 1 | 1 | 1 | 1 | 1 | 2 | 2 | 2 | 2 | 2 | 3 | 3
Total (8 hrs operations) |  | 3 | 3 | 6 | 7 | 9 | 9 | 10 | 12 | 12 | 14 | 17 | 17 | 20 | 22
Daily Capacity (8hr operations) |  | 56 | 112 | 168 | 224 | 280 | 336 | 392 | 448 | 504 | 560 | 616 | 672 | 728 | 784
Team Leader to cover as Results Recorder for small sites
** Queue Coordinator requirements are particularly indicative and should be determined on a site by site basis, dependent on site specific requirements and local infrastructure
Note: Assumes all Participants to use self-swab. For minors and those unable to self-swab, assumes a guardian or career will assist with swabbing
Note: Assumes sufficient workforce to deliver 70% capacity
Note: Additional contingency resource has been added to cover breaks and potential absences. It is recommended that staff rotate across multiple positions throughout the day, with breaks and all staff provided equal break time
REQUIREMENTS PER 70% CAPACITY TESTING SITE SIZE (1/2)
The table below outlines the indicative number of staff needed to operate a testing site per shift to 70% capacity
This is based off an 8 hour day and a 7 throughput per testing station per hour
Additional contingency resource has been added to cover breaks and potential absences
It is recommended that staff rotate across multiple positions throughout the day, with breaks (all staff provided equal break time), to maintain energy levels and reduce risk of human error
Workforce numbers are a guideline only and local decisions should be made on a sensible workforce size on a site by site basis.

## Slide 188
 |  | Number of Testing Stations (Testing Site Size) |  |  |  |  |  |  |  |  |  |  |  |  | 
Role | Position | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28
Team Leader |  | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
Site Operations Role | Queue Coordinator** | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 2 | 2
 | Registration Assistant | 2 | 2 | 2 | 3 | 3 | 3 | 3 | 3 | 4 | 4 | 4 | 4 | 4 | 4
 | Test Assistant*** | 3 | 3 | 3 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 5 | 5 | 5
Testing Operations Role | Processing Operative | 11 | 11 | 12 | 13 | 13 | 14 | 15 | 15 | 16 | 17 | 18 | 18 | 19 | 20
 | Results Recorder | 2 | 3 | 3 | 3 | 3 | 3 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4
Break & Absence Cover (8 hrs operations) |  | 3 | 3 | 3 | 4 | 4 | 4 | 4 | 4 | 5 | 5 | 5 | 5 | 5 | 5
Total (8 hrs operations) |  | 23 | 24 | 25 | 29 | 29 | 30 | 32 | 32 | 35 | 36 | 37 | 38 | 40 | 41
Daily Capacity (8hr operations) |  | 840 | 896 | 952 | 1008 | 1064 | 1120 | 1176 | 1232 | 1288 | 1344 | 1400 | 1456 | 1512 | 1568
PER 70% CAPACITY TESTING SITE SIZE (2/2)
Team Leader to cover as Results Recorder for small sites
** Queue Coordinator requirements are particularly indicative and should be determined on a site by site basis, dependent on site specific requirements and local infrastructure
Note: Assumes all Participants to use self-swab. For minors and those unable to self-swab, assumes a guardian or career will assist with swabbing
Note: Assumes sufficient workforce to deliver 70% capacity
Note: Additional contingency resource has been added to cover breaks and potential absences. It is recommended that staff rotate across multiple positions throughout the day, with breaks and all staff provided equal break time
The table below outlines the indicative number of staff needed to operate a testing site per shift to 70% capacity
This is based off an 8 hour day and a 7 throughput per testing station per hour
Additional contingency resource has been added to cover breaks and potential absences
It is recommended that staff rotate across multiple positions throughout the day, with breaks (all staff provided equal break time), to maintain energy levels and reduce risk of human error
Workforce numbers are a guideline only and local decisions should be made on a sensible workforce size on a site by site basis.

## Slide 189
 |  | Number of Testing Stations (Testing Site Size) |  |  |  |  |  |  |  |  |  |  |  |  | 
Role | Position | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14
Team Leader |  | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
Site Operations Role | Queue Coordinator** | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
 | Registration Assistant | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 1
 | Test Assistant*** | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 2
Testing Operations Role | Processing Operative | 1 | 1 | 1 | 2 | 2 | 2 | 3 | 3 | 4 | 4 | 4 | 5 | 5 | 6
 | Results Recorder | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
Break & Absence Cover (8 hrs operations) |  | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 2
Total (8 hrs operations) |  | 3 | 3 | 3 | 5 | 5 | 6 | 7 | 8 | 9 | 9 | 9 | 10 | 10 | 13
Daily Capacity (8hr operations) |  | 32 | 64 | 96 | 128 | 160 | 192 | 224 | 256 | 288 | 320 | 352 | 384 | 416 | 448
Team Leader to cover as Results Recorder for small sites
** Queue Coordinator requirements are particularly indicative and should be determined on a site by site basis, dependent on site specific requirements and local infrastructure
Note: Assumes all Participants to use self-swab. For minors and those unable to self-swab, assumes a guardian or career will assist with swabbing
Note: Assumes sufficient workforce to deliver 40% capacity per bay
Note: Additional contingency resource has been added to cover breaks and potential absences. It is recommended that staff rotate across multiple positions throughout the day, with breaks and all staff provided equal break time
PER 40% CAPACITY TESTING SITE SIZE (1/2)
Workforce numbers are a guideline only and local decisions should be made on a sensible workforce size on a site by site basis.
The table below outlines the indicative number of staff needed to operate a testing site per shift to 40% capacity
This is based off an 8 hour day and a 4 throughput per testing station per hour
Additional contingency resource has been added to cover breaks and potential absences
It is recommended that staff rotate across multiple positions throughout the day, with breaks (all staff provided equal break time), to maintain energy levels and reduce risk of human error

## Slide 190
 |  | Number of Testing Stations (Testing Site Size) |  |  |  |  |  |  |  |  |  |  |  |  | 
Role | Position | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28
Team Leader |  | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
Site Operations Role | Queue Coordinator** | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
 | Registration Assistant | 1 | 1 | 1 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2
 | Test Assistant*** | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 3 | 3 | 3
Testing Operations Role | Processing Operative | 6 | 6 | 7 | 7 | 8 | 8 | 8 | 9 | 9 | 10 | 10 | 10 | 11 | 11
 | Results Recorder | 1 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2
Break & Absence Cover (8 hrs operations) |  | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 3 | 3 | 3 | 3 | 3
Total (8 hrs operations) |  | 13 | 14 | 15 | 16 | 17 | 17 | 17 | 18 | 18 | 20 | 20 | 21 | 22 | 22
Daily Capacity (8hr operations) |  | 480 | 512 | 544 | 576 | 608 | 640 | 672 | 704 | 736 | 768 | 800 | 832 | 864 | 896
PER 40% CAPACITY TESTING SITE SIZE (2/2)
Team Leader to cover as Results Recorder for small sites
** Queue Coordinator requirements are particularly indicative and should be determined on a site by site basis, dependent on site specific requirements and local infrastructure
Note: Assumes all Participants to use self-swab. For minors and those unable to self-swab, assumes a guardian or career will assist with swabbing
Note: Assumes sufficient workforce to deliver 40% capacity
Note: Additional contingency resource has been added to cover breaks and potential absences. It is recommended that staff rotate across multiple positions throughout the day, with breaks and all staff provided equal break time
Workforce numbers are a guideline only and local decisions should be made on a sensible workforce size on a site by site basis.
The table below outlines the indicative number of staff needed to operate a testing site per shift to 40% capacity
This is based off an 8 hour day and a 4 throughput per testing station per hour
Additional contingency resource has been added to cover breaks and potential absences
It is recommended that staff rotate across multiple positions throughout the day, with breaks (all staff provided equal break time), to maintain energy levels and reduce risk of human error

## Slide 191: APPENDIX: TRAINING FAQS

## Slide 192: TRAINING: FAQS 1
QUESTION | ANSWER
Workforce training and support provided? | The online training platform will help train staff to safely process samples. We’ll also provide a guidebook and Standard Operating Procedure SOP which covers important aspects of site operations which should form part of staff training, including - infection prevention and control measures, cleaning protocols, and appropriate use of PPE in full.
What if I can’t log in to the training? | Any person who is not able to log in should check if they have the correct login details with the test coordinator / supervisor and retry to login. If the problem still exists then, an email can be sent to the learning platform administrators via the shared DHSC email ID provided to the testing coordinator/supervisor.
Can I take the training multiple times? | Yes – although the training should be repeated only when the duration between the last date when the training was taken is significant or when the role of the tester has changed since the last training date.
What is available for us to use? | We have an online training platform which is to be used across the tester workforce in the United Kingdom. The online training is for individuals to use the Lateral Flow Device (LFD) deployed by NHS Test and Trace.
How long does the training take? | This will depend how many modules are needing to be taken, which is linked to which role a person is doing. Each module takes approx. 15mins, 10mins reading and 5 mins assessment.
What does the training consist of? | Each module contains 2 sections, 1) information and guidance consisting of written text and videos 2) Assessment via multiple choice questions.
Is there a pass or fail? What if someone fails? | Yes, each person must achieve 100% in the assessment. They are able to retake each module if they do not achieve this.
How do I access it? | The training is hosted online and the Senior Responsible Officer (SRO) and team Leader of each local authority will receive the link and token, then the SRO/Team Leader will circulate among their teams.
Can I organise my own training? | No. All training has been developed in line with Clinical Standard Operating Procedures and is regularly updated to ensure that the training is accurate and consistent.

## Slide 193: TRAINING: FAQS 2
QUESTION | ANSWER
Is the training available in other languages? | The training content e.g. videos will be available in Welsh and we are considering whether training materials should be available in some of the most commonly spoken other languages.
Does the training support assistive technologies? | We are working to include sub-titles on all videos to help those with hearing difficulties. Transcripts are provided for all videos.
Can I host the training on my own LMS? (learning management system) | No. The courses/modules cannot be hosted on to other LMS systems because this would break the connectivity to report who has completed the modules and who has passed the assessments.
Is any non-IT based training available? | Everything developed to-date has been IT based. However, some of the PDF documents can be downloaded for use. We are also looking at developing Zoom sessions where people can ask frequently asked questions (FAQs).
Are there other training materials/reference documents to support the online training? | Yes, whilst the online training platform will help train staff to safely process samples. We’ll also provide guidebook and the SOP which cover important aspects of site operations which should form part of staff training, including - Infection prevention and control measures, cleaning protocols, and appropriate use of PPE etc. There are also several written resources which can be downloaded and accessed offline for reference.
How much does the training cost? | The training is a DHSC resource and is free to access.
When am I required to complete the online training? | You are required to complete the online training before entering the testing site for practical training.
What if I don’t have access to a computer to complete my online training? | If this is the case, please reach out to your team leader and they will provide you with a solution.
Who should take the training? | Anyone who will be involved in the testing process should take the training.

## Slide 194: TRAINING: FAQS 3
QUESTION | ANSWER
What’s the total user capacity of the training platform? | Training platform can accommodate up to 120K users but we are working to get this number increased.
What’s the total concurrency capacity of the training platform? | 2,400 users can access/train at one time. This is being monitored and can be increased if we notice problems with concurrency.
Do you offer additional training to help us reach under-represented groups for example? | We recognise that the best way to undertake this exercise is to be led locally, as LA’s know their areas best and now which groups are prevalent within their regions. Therefore it is up to LA’s to reach out to their local networks to ensure these groups are tested. As explained above, you may wish to train your workforce on cultural awareness as appropriate for your local area.
Can the training be accessed on personal devices? | Yes, a person needs the web address and token code in order to be able to commence training.
Once a person completes the online training, are they competent to begin work? | No, there are further practical elements that need to be completed. This is explained in the blueprint document.
Do staff need qualifications to undergo the training? | No, the training is suitable for all, see job roles for more specific recommendations for suitable team members.
Are we liable if a test is incorrectly administered, potentially resulting in an injury ie nose bleed? | It is recommended that all sites conduct a thorough risk assessment in line with their own health and safety policy and appropriate insurances.
Can your training platform cope if all Tier 3 LA’s need to go-live quickly? | Our system has been robustly tested and can accommodate up to 120K users but we are working to get this number increased in time for the 3rd December.